## Slide 1: Routing and Wavelength Assignment Information Model for Wavelength Switched Optical Networks
Young Lee ylee@huawei.com
Huawei
Greg Bernstein gregb@grotto-networking.com Grotto Networking
draft-ietf-ccamp-wson-info-08.txt

## Slide 2: Authors/Contributors
Greg Bernstein (Grotto Networking)
Diego Caviglia (Ericsson)
Ander Gavler (Acreo AB)
Young Lee (Huawei)
Dan Li (Huawei)
Wataru Imajuku (NTT)
Jonas Martensson (Acreo AB)
Itaru Nishioka (NEC Corp.)
? Giovanni?, ? Pierre?

## Slide 3: Changes
Changes from 07
  Added shared fiber connectivity to resource pool modeling. This includes information for determining wavelength collision on an internal fiber providing access to resource blocks. (This is a WSON specific change and does not impact general constraint encoding)

## Slide 4: Existing OEO Pool Model
Resource block containing one or more identical resource that have identical “access”
Ingress and Egress connection matrices to specify “access” to the blocks
I1 +-------------+ +-------------+ E1
----->| | +--------+ | |----->
I2 | +------+ Rb #1 +-------+ | E2
----->| | +--------+ | |----->
| | | |
| Resource | +--------+ | Resource |
| Pool +------+ +-------+ Pool |
| | + Rb #2 + | |
| Ingress +------+ +-------| Egress |
| Connection | +--------+ | Connection |
| Matrix | . | Matrix |
| | . | |
| | . | |
IN | | +--------+ | | EM
----->| +------+ Rb #P +-------+ |----->
| | +--------+ | |
+-------------+ +-------------+
Figure 1 Schematic diagram of resource pool model.
Only simple wavelength constraints here no state
Only state, if any, associated with resources in pool

## Slide 5: Issue in modeling OEO pools
Initially looked just like previous situation, but…
From node A
From node B
From node C
To node A
To node B
To node C
add
drop
…
…
Tun.
Drop
Tun.
Drop
OEO pool
These are single fibers shared by all wavelengths on ingress or egress
Figure & Example from Pierre Peloso and Giovanni Martinelli

## Slide 6: Enhanced OEO pool Model
Add option for resource block access to be via a shared medium (fiber)
Add wavelength availability state information for the shared fibers
I1 +-------------+ +-------------+ E1
----->| | +--------+ | |----->
I2 | +======+ Rb #1 +=======+ | E2
----->| | +--------+ | |----->
| | | |
| Resource | +--------+ | Resource |
| Pool | | Pool | | |
| |======+ Rb #2 +=======+ |
| Ingress | + | | Egress |
| Connection | +--------+ | Connection |
| Matrix | . | Matrix |
| | . | |
| | . | |
IN | | +--------+ | | EM
----->| +======+ Rb #P +=======+ |----->
| | +--------+ | |
+-------------+ +-------------+
Can be a shared fiber. Hence need wavelength state info

## Slide 7: Small Additions to Model
Resource Pool State
  <ResourcePoolState>::=(<ResourceBlockID> <NumResourcesInUse> <InAvailableWavelengths> <OutAvailableWavelengths> )...
Resource Block Info
  <ResourceBlockInfo> ::= ([<ResourceSet>] <InputConstraints> <ProcessingCapabilities> <OutputConstraints>)*  no change
  <InputConstraints> ::= <SharedIngress> <ModulationTypeList> <FECTypeList> <BitRateRange> <ClientSignalList>
  <OutputConstraints> := <SharedEgress> <ModulationTypeList> <FECTypeList>

## Slide 8: Next Steps
Any more comments?
Prepare for last call