## Slide 1: GMPLS Signaling Extensions for the Evolving G.709 OTN Control
CCAMP WG, IETF 78th, Maastricht, Netherlands
draft-zhang-ccamp-gmpls-evolving-g709-05.txt
Fatai Zhang <zhangfatai@huawei.com>
Guoying Zhang <zhangguoying@mail.ritt.com.cn>
Sergio Belotti <sergio.belotti@alcatel-lucent.it>
Daniele Ceccarelli <daniele.ceccarelli@ericsson.com>

## Slide 2: Changes from Version 04
Tributary Port Number (TPN) assignment by control plane is introduced in this new version
  Auto-MSI is deprecated by G.798
  Added a section to introduce a new TPN object and describe the procedure of TPN assignment

## Slide 3: TPN in Data Plane
TPN is carried by N MSI bytes in the OPUk overhead
  N = the total number of TS
  Each byte indicates the multiplex structure of one TS
  One TPN is assigned for the same LO ODUj in each OTUk link
……
TPN = 2
TPN = 3
……
OTU3 link
OTU3 link
B
A
TPN = 2
MSI [i] | LO ODU | TPN
#1 | ODU2 | 2
#2 | ODU2 | 2
#3 | ODU1 | x
#4 | ODU1 | y
#5 | ODU2 | 2
#6 | ODU2 | 2
#7 ~ #16 | Others | Others
MSI bytes in OPUk OH
C
TPN = 3

## Slide 4: TPN Assignment by Control Plane
……
OTU3 link
B
A
……
OTU3 link
C
Path: Req ODU2
Resv: Label = #2/4/5/6, TPN = 3
Resv: Label = #1/2/5/6, TPN = 2
Path: Req ODU2
……
OTU3 link
B
A
……
OTU3 link
C
Path: Label = #1/2/5/6, TPN = 2
Resv: accept
Resv: accept
Path: Label = #2/4/5/6, TPN = 3
Downstream Assignment
Upstream Assignment
Auto-MSI (data plane TPN assignment) is deprecated by G.798, so Control Plane TPN assignment is needed

## Slide 5: New Object for TPN
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|D| Reserved | TPN |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
A new TPN object is introduced in the PATH and/or RESV message to support TPN assignment
D bit: indicate downstream or upstream TPN assignment
TPN (16 bits): the assigned TPN value

## Slide 6: Next Steps
Adopt it as a WG document
  Many people are interested in this topic
  Significant agreement have been achieved
  Quite stable for quite long time
Investigate the possibility to put TPN information into Label object
Refine it according to the feedback from the meeting or mailing list