## Slide 1: GMPLS-based Hierarchy LSP creation in MRN/MLN
CCAMP WG, IETF 78th, Maastricht, Netherlands
draft-zhang-ccamp-gmpls-h-lsp-mln-01.txt
Fatai Zhang <zhangfatai@huawei.com>
Dan Li <danli@huawei.com>

## Slide 2: Motivations
In MLN/MRN:
  There may be multiple switching capabilities in the server layer network: (Named as MRN in RFC5212)
    E.g., PSC, TDM/SDH, TDM/OTN, WDM…(identified by ISC)
  There may be multiple switching granularities for one switching capability (data plane switching layers of the same ISC)
    E.g., VCxx in SDH, ODUj in OTN…
The term MLN is general, referring to a layered network, which may consist of either single or multiple regions (RFC5212)
When creating Hierarchy LSP through multi-layer network, the performance of selection of server layer switching capability & granularity is necessary

## Slide 3: Multi-Server Layer Selection
For hybrid node, one interface may have multiple Switching Capabilities (SC), so there may be multiple SC choices for FA-LSP
PSC
PSC
PSC
PSC
TDM
WDM
TDM
WDM
TDM
WDM
FA-LSP
PSC FA
Link with TDM & WDM SCs
Internal link
FA
TDM & WDM
TDM & WDM
FA-LSP
Node A
Node B
Node C
Node D
Node E
Client Layer LSP
Client layer LSP
Client layer link
draft-ietf-ccamp-gmpls-mln-extensions-12 provides an SC sub-object in XRO (in the PATH message for the client layer LSP) to exclude SCs not to be used, which indicates the selected SC impliedly (but it is not straightforward)

## Slide 4: Multi-Granularity Selection
PSC
PSC
PSC
PSC
TDM
TDM
TDM
FA
FA-LSP
Node A
Node B
Node C
Node D
Node E
Client Layer LSP
OTU3
OTU3
TDM
TDM
TDM
TDM
FA
FA-LSP
Node A
Node B
Node C
Node D
Node E
ODU0
OTU3
OTU3
TDM
Multi-choices:
ODU1 / 0DU2 / 0DU3
Multi-choices:
ODU1 / 0DU2 / 0DU3
Case1: Multi-Region Network
Case2: Multi-Layer Network in same Region
Even when there is only one SC in server layer, there may be still multiple choices of server layer switching granularities for FA-LSP

## Slide 5: Signaling Extension
PSC
PSC
PSC
PSC
TDM
TDM
TDM
PSC FA
FA-LSP
Node A
Node B
Node C
Node D
Node E
Client Layer LSP
OTU3
OTU3
IF_p1
IF_t1
IF_t2
IF_p2
IF_p1
IF_t1
IF_t2
IF_p2
ODU2
ODU2
ERO =
PATH: server SC = TDM, granularity = ODU2
If the source node of the client layer LSP performs the full inter-layer path computation, the client layer PATH message needs to indicate the edge node the path information of the server layer FA-LSP
Extension: Added a new Server_Layer_Info sub-object in ERO
  Indicate the server layer SC and granularity

## Slide 6: Sub-Object Format
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|L| Type | Length |M| Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| LSP Enc. Type |Switching Type | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Traffic Parameters |
~ ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
LSP Encoding Type & Switching Type: Indicate the selected server layer switching capability
Traffic Parameters: Indicate the selected server layer switching granularity (e.g., VC3/VC4…)
M bit: Indicate such selection is mandatory or not
The format of Server_Layer_Info sub-object in ERO:

## Slide 7: Next Steps
Comments are always appreciated
Refine it according to the feedback from the meeting or mailing list