## Slide 1: RSVP-TE Extension for Multi Stages Multiplexing Configuration in G.709 network
    draft-fuxh-ccamp-multi-stage-multiplex-config-rsvp-01
Xihua Fu, Malcolm Betts, ZTE Corporation
Ruiquan Jin, Xiaoli Huo, China Telecom
Yunbin Xu, CATR

## Slide 2: RSVP-TE Extension Requirement for Multi Stages Multiplexing (MSM) Configuration
Some nodes at a limited number of places in the network support different multiple MSM hierarchies for ODUi being mapped into ODUk (k>i) (e.g., ODU0-ODU1-ODU3 and ODU0-ODU2-ODU3).
If path computation entity select the ODU0-ODU2-ODU3 in Node B and C for e2e ODU0 service from A to Z, there has to be an ODU2 tunnel between B and C.
ODU0-ODU2-ODU3 multiplexing hierarchy has to be carried in signaling message. Node B will triggered a creation of an ODU2 FA-LSP. Node B and C must configure this kind of MSM hierarchy (i.e., ODU0-ODU2-ODU3) to its data plane who can know how ODU0 signal can be mapped and demapped.

## Slide 3
The ERBO (Explicit Route Boundary Object) in PATH message, was defined in [draft-fuxh-ccamp-boundary-explicit-control-ext-00].
  It has ever been presented in 76th and 77th meeting in CCAMP and PCE.
    http://www.ietf.org/proceedings/76/slides/ccamp-28/ccamp-28.htm
    http://www.ietf.org/proceedings/77/slides/pce-13/pce-13_files/v3_document.htm
It is used for the explicitly control hierarchy LSP creation. ERBO has the same format as the ERO.
Explicit Route Boundary Control

## Slide 4
This document introduce a new sub-object (HOP_ATTRIBUTES) carry the attributes of the associated hop specified in the ERBO.
  It allows the specification and reporting of attributes relevant to a particular hop of the signaled LSP.
  It follows an IPv4 or IPv6 prefix or unnumbered Interface ID sub-object in ERBO.
A list of attribute TLV can be inserted into ERBO. These attributes may represents the following information. It can be further extended to carry other specific requirement in the future.
  Server Layer (e.g., PSC, L2SC, TDM, LSC, FSC) or Sub-Layer (e.g., VC4, VC11, VC4-4c, VC4-16c, VC4-64c, ODU1, ODU2, ODU3, ODU4) used for boundary node to trigger one specific corresponding server layer or sub-layer FA-LSP creation.
  Multiplexing hierarchy (e.g., ODU0-ODU1-ODU3-ODU4) used for boundary node to configure it to the data plane and trigger one specific corresponding tunnel creation.
HOP_ATTRIBUTE

## Slide 5
Lower Layer Attribute TLV
  It indicates boundary node should trigger one corresponding server layer or sub-layer FA-LSP creation which is defined in the attribute TLV.
  Server Layer: Indicates which corresponding server layer should be triggered by the boundary node. The value of server layer is the same as the switching capability [RFC3471]
  Sub Layer: If there are several sub-layers within one server layer, it can further indicates which sub layer should be triggered by the boundary node.
    SDH/SONET: VC4, VC11, VC12, VC4-4c, VC4-16c, VC4-64c
    ODUk: ODU1, ODU2, ODU3, ODU2e, ODU4, …
  Stitching or nesting flags should be set in terms of [RFC5151]
Attribute TLV

## Slide 6
Multiplexing Hierarchy Attribute TLV
  In following figure, the server layer and sub-layer information is not enough for data plane to know ODU0 is mapped into ODU3 tunnel by ODU0-ODU1-ODU3 then ODU4.
  It indicates the multiplexing hierarchies (e.g., ODU0-ODU1-ODU3-ODU4) used for boundary node to configure it to the data plane and trigger one specific corresponding tunnel creation.
Attribute TLV

## Slide 7
F: 0 (Inclusive Multiplexing Hierarchies), 1 (Exclusive Multiplexing Hierarchies)
Number:total nunmbers of multiplexing hierarchies which are supported by one interface.
MSMH 1, MSMH2, ... , MSMH M (4 bits): Indicates the numbers of Multi Stages Multiplexing Hierarchies (MSMH).
  MSMH = 1: It indicates ODUi is mapped into ODUk (k > i) by single stage multiplexing (e.g., ODU0-ODU3).
  MSMH > 1: It indicates ODUi is mapped into ODUk (k > i) by multi stages multiplexing (e.g., ODU0-ODU1-ODU3, MSMH = 2).
MSMC 1, MSMC 2, ... ,MSMC M: Indicates the detailed information of multi stages multiplexing hierarchy. The length of MSMC is (MSMH+1) * 4. Each ODUk (k=1, 2, 3, 4, 2e, flex) is indicated by 4 bits.
  Value Type
  0000 ODU0
  0001 ODU1
  0010 ODU2
  0011 ODU3
  0100 ODU4
  0101 ODU2e
  0110 ODUflex
  7-15 Reserved (for future use)
Attribute TLV

## Slide 8: Example: ERBO, HOP-ATTRIBUTE
HOP_ATTRIBUTE follows the unnumber interface ID and includes one Lower Layer attribute TLV and one Multiplexing Hierarchy attribute TLV.

## Slide 9: Example: Signalling procedure for Multi Stages Multiplexing Configuration

## Slide 10: Next Steps
Refine the document according the feedback of meeting and mailing list