## Slide 1: Information Modele Electro-Optical Multi-Layer G.709 network
    draft-xie-ccamp-multi-elec-opt-network-ext-req-00
Gand Xie, Xihua Fu, ZTE Corporation

## Slide 2: Information requirement for path computation in electro-optical multi-layer network
Motivation
There four paths for LSP which from A to D:
  A-B-C-D, A-B-C-F-D, A-E-F-D, A-E-F-C-D;
Modulation type of interface
  If-2 and If-8 is DPSK,;
  If-11 is DQPSK;
  In node C, some internal link is DPSK, others is DQPSK
So
  A-E-F-D is not used;
  A-B-C-F-D and A-E-F-C-D are not sure to be used;

## Slide 3: Information requirement for path computation in electro-optical multi-layer network
WSON information
  Connectivity matrix;
  Resource Pool for wavelength converter or regeneration;
No electro-optical constraint information for add port and drop port;

## Slide 4: Information Model for Multi-Layer G.709
Information extension
Key devices of electro-optical conversion: optical transmitter and optical receiver;
Characteristic of optical transmitter:
  Tunable;
  Tuning range;
  Tuning time;
  Modulation type;
  FEC type;
  Signal type;
Characteristic of optical receiver:
  Tunable;
  Tuning range;
  Tuning time;
  Modulation type;
  FEC type;
  Signal type;
Every characteristic is optional.

## Slide 5: Information Model for Multi-Layer G.709
Infor Model: scenario 1:
Information of Link end with optical transmitter and optical receiver:
  <Link Info>::=<ISCD><Wavelength tunable capability><Signal process capability>
Info Model: scenario 2:
Internal link is a unique identifier of add port, drop port, optical transmitter and optical receiver.
<Node Info>::=<Internal link list>
  <Internal link>::=<Link ID><Wavelength tunable capability><Signal processing capability>

## Slide 6: Information Model for Multi-Layer G.709
Info Model for hybrid node
Internal link
  Internal link 31: drop 21, add 23, optical receiver 1, optical transmitter 1;
  Internal link 32: drop 22, add 24, optical receiver 2, optical transmitter 2;
<Node Info>::=<Internal link 31><Internal link 32>
  <Internal link 31>::=<Link ID(31)><Wavelength tunable capability><Signal processing capability(DPSK)>
  <Internal link 32>::=<Link ID(32)><Wavelength tunable capability>< Signal processing capability(DQPSK)>

## Slide 7: Information Model for Multi-Layer G.709
Extension for single-switching-type-node:
Optical transmitter and optical receiver at If-2, if-8 and if-11;
Information extension:
  <Link info(if-2)>::=<ISCD(LSC)><Wavelength tunable capability><Signal processing capability(DPSK)>
  <Link info(if-8)>::=<ISCD(LSC)><Wavelength tunable capability>< Signal processing capability(DPSK)>
  <Link info(if-11)>::=<ISCD(LSC)><Wavelength tunable capability>< Signal processing capability(DQPSK)>
Usable paths:
Path1: A.1-B.2-B.3-C.4(-C.31)-C.5-D.6;
Path2: A.1-B.2-B.3-C.4(-C.31-C.32)-C.13-F.14-F.11-D.6;
Path3: A.7-E.8-E.9-F.10-F.14-C.13(-C.31)-C.5-D.6;

## Slide 8: Protocol Extension Requiement for Mult-Layer in OTN
Extending Requirement protocols
  OSPF or ISIS need be extended;
  Signal protocol need be extend to inform the internal link when LSP is creating;
  PCEP protocol need be extended to inform the internal link when PCE is used for path computation;

## Slide 9: Next Steps
Refine the document according the feedback of meeting and mailing list