## Slide 1: LSP Attributes Related Routing Backus-Naur Form draft-berger-ccamp-attribute-bnf-00
Editors:
Lou Berger <lberger@labn.net>
George Swallow <swallow@cisco.com>

## Slide 2: Draft Motivation
Clarify usage of RFC5420’s LSP_ATTRIBUTES and LSP_REQUIRED_ATTRIBUTES Objects
  In Path and Resv messages
BNF not included in RFC5420
  Narrative leaves room for interpretation, particular impact to P2MP LSPs (RFC4875)
  Some have proposed using RRO as a solution, or constructing P2MP SL2s to avoid the problem
Potential Applicability
  draft-ietf-mpls-rsvp-te-no-php-oob-mapping
  draft-ietf-ccamp-oam-configuration-fwk-03

## Slide 3: RFC5420 Objects
LSP_ATTRIBUTES class = 197, C-Type = 1
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
// Attributes TLVs //
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
LSP_REQUIRED_ATTRIBUTES class = 67, C-Type = 1
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
// Attributes TLVs //
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 4: RFC5420 Path Message Narrative
Objects MAY be carried in Path messages
Ordering is not significant (as is typical RSVP)
  MUST allow for any order
Objects SHOULD be after the SESSION_ATTRIBUTE object or, when not present, after the LABEL_REQUEST object
LSP_REQUIRED_ATTRIBUTES object should come before LSP_ATTRIBUTES object
Only 1st object per class is significant
  Other instances SHOULD be ignored and MUST be forwarded unchanged

## Slide 5: Proposed Matching BNF
<Path Message> ::= <Common Header> [ <INTEGRITY> ]
[ [<MESSAGE_ID_ACK> | <MESSAGE_ID_NACK>] ...]
[ <MESSAGE_ID> ]
<SESSION> <RSVP_HOP>
<TIME_VALUES>
[ <EXPLICIT_ROUTE> ]
<LABEL_REQUEST>
[ <PROTECTION> ]
[ <LABEL_SET> ... ]
[ <SESSION_ATTRIBUTE> ]
[ <LSP_REQUIRED_ATTRIBUTES> ... ]
[ <LSP_ATTRIBUTES> ... ]
[ <NOTIFY_REQUEST> ]
[ <ADMIN_STATUS> ]
[ <POLICY_DATA> ... ]
<sender descriptor>
[<S2L sub-LSP descriptor list>] /* from RFC4875 */

## Slide 6: RFC5420 Resv Message Narrative
ATTRIBUTE Objects MAY be carried in Resv messages
Ordering is not significant within a flow descriptor
  MUST allow for any order, subject to the following
Objects are part of the flow descriptor, i.e., MUST follow a FILTER_SPEC.
  Object SHOULD follow immediately after the LABEL object.
Only 1st object is significant per flow descriptor
  Other instances SHOULD be ignored and MUST be forwarded unchanged
Note: reporting is per LSP not per P2MP SL2/desination

## Slide 7: Proposed Matching BNF – Per LSP
<FF flow descriptor list> ::= <FF flow descriptor>
[ <FF flow descriptor list> ]
<FF flow descriptor> ::= [ <FLOWSPEC> ] <FILTER_SPEC> <LABEL>
[ <LSP_ATTRIBUTES> ... ]
[ <RECORD_ROUTE> ]
[ <S2L sub-LSP flow descriptor list> ]
<SE flow descriptor> ::= <FLOWSPEC> <SE filter spec list>
<SE filter spec list> ::= <SE filter spec>
[ <SE filter spec list> ]
<SE filter spec> ::= <FILTER_SPEC> <LABEL>
[ <LSP_ATTRIBUTES> ... ]
[ <RECORD_ROUTE> ]
[ <S2L sub-LSP flow descriptor list> ]

## Slide 8: P2MP Per Destination Attributes
What about reporting per P2MP destination (S2L) ATTRIBUTE objects?
  RFC5420 allows reporting when all destinations have the same object values, what about when they don’t?
Proposed Solution – Narrative
  To report attributes per destination:
  LSP_ATTRIBUTES objects MUST follow a S2L_SUB_LSP object
  Only 1st object is significant per S2L
    Other instances SHOULD be ignored and MUST be forwarded unchanged

## Slide 9: Proposed Matching BNF – Per S2L
<FF flow descriptor> ::= [ <FLOWSPEC> ] <FILTER_SPEC> <LABEL>
[ <RECORD_ROUTE> ]
[ <S2L sub-LSP flow descriptor list> ]
<SE filter spec> ::= <FILTER_SPEC> <LABEL>
[ <RECORD_ROUTE> ]
[ <S2L sub-LSP flow descriptor list> ]
<S2L sub-LSP flow descriptor list> ::=
<S2L sub-LSP flow descriptor>
[ <S2L sub-LSP flow descriptor list> ]
<S2L sub-LSP flow descriptor> ::= <S2L_SUB_LSP>
[ <LSP_ATTRIBUTES> ... ]
[ <P2MP_SECONDARY_RECORD_ROUTE> ]

## Slide 10: Compatibility
Non-supporting nodes will interpret the 1st S2L ATTRIBUTE object as applying to the LSP
As current P2MP implementations only have per LSP reporting is same as today
  Today’s implementations that need reporting per destination, limit one destination per Path
    See draft-ietf-mpls-rsvp-te-no-php-oob-mapping
 No harm, but also no value

## Slide 11: Next steps
Gauge general interest
Address comments
Comments?