## Slide 1: A Framework for the Control and Measurement of Wavelength Switched Optical Networks (WSON) with Impairments
IETF 78th Maastricht, Netherlands, July 2010
Young Lee ylee@huawei.com
Huawei
Greg Bernstein gregb@grotto-networking.com Grotto Networking
Dan Li danli@huawei.com
Huawei
Giovanni Martinelli giomarti@cisco.com
Cisco
draft-ietf-ccamp-wson-impairments-03.txt

## Slide 2: Contributors
IETF 78th Maastricht, Netherlands, July 2010
Ming Chen (Huawei)
Gabriele Galimberti (Cisco)
Rebecca Han (Huawei)
Alberto Tanzi (Cisco)

## Slide 3: A Framework for WSONs with Impairments
IETF 78th Maastricht, Netherlands, July 2010
Scope
  This document discusses how the definition and characterization of optical fiber, devices, subsystems, and network elements contained in various ITU-T recommendations can be combined with GMPLS control plane protocols and mechanisms to support Impairment Aware Routing and Wavelength Assignment (IA-RWA) in optical networks.

## Slide 4: Updates
IETF 78th Maastricht, Netherlands, July 2010
Changes from 01 to 02:
  Correct and refine use of "black link" concept based on liaison with ITU-T and WG feedback.
Changes from 02 to 03:
  Insert additional information on use and considerations for regenerators in section 3.

## Slide 5: “Black Links” and the Control Plane
  In GMPLS, information used for path computation is standardized for distribution amongst the elements participating in the control plane. For optical systems this may not be possible.
  This is due to only portions of an optical system being subject to standardization. These DWDM links are referred to as "black links" since their details are not generally available.
  From the control plane point of view this restricts information flow and computation architecture choices.
IETF 78th Maastricht, Netherlands, July 2010

## Slide 6: Refined “Black Link Options”
The authority in control of the "black links"
  can furnish a list of all viable paths between all viable node pairs to a computational entity.
  could provide a PCE like entity that would furnish a list of viable paths/wavelengths between two requested nodes.
  can provide a PCE that performs full IA-RWA services.
IETF 78th Maastricht, Netherlands, July 2010
Thanks to Peter Anslow for suggesting revisions to our text

## Slide 7: Regenerator Enhancement
IETF 78th Maastricht, Netherlands, July 2010
In the latter case a lightpath can be seen as a set of transparent segments. The optical impairments calculation needs to be reset at each regeneration point so each transparent segment will have its own impairment evaluation.
+---+ +----+ +----+ +---+ +----+ +---+
| I |----| N1 |---| N2 |-----| R |-----| N3 |----| E |
+--+ +----+ +----+ +---+ +----+ +---+
|--------------------------|------------------|
Segment 1 Segment 2
Lightpath as a set of transparent segments
For example, Figure 1 represents a lightpath from node I to node E with a regeneration point R in between. The lightpath is from an impairment validation perspective if each segment (I, N1, N2, R) and (R, N3, E) is feasible.

## Slide 8: Next Steps/Issues
IETF 78th Maastricht, Netherlands, July 2010
Refine alternatives based on refined black link concepts.
Refine approximation models.
Restart work on follow on drafts (if sufficient interest ☺)
  Information Model and Encoding for impairments.
  Protocol specific solutions.