## Slide 1: OSPF Extensions in Support of Impairment Aware Routing and Wavelength Assignment in Wavelength Switched Optical Networks
CCAMP WG, IETF 78th, Maastricht, Netherlands
draft-agraz-ccamp-wson-impairment-ospf-00.txt
Fernando Agraz (agraz@tsc.upc.edu)
Yabin Ye (yabin.ye@huawei.com)
Notes: <number>

## Slide 2: Acknowledgments
This work is supported by DICONET (Dynamic Impairment Constraint Networking for Transparent Mesh Optical Networks) project under FP7/2007-2013 - GA nr 216338
Contributors
  Chava Vijaya Saradhi CREATE-NET
  Email: saradhi.chava@create-net.org
  Antonio Francescon CREATE-NET
  Email: antonio.francescon@create-net.org

## Slide 3: Background
Full name： Dynamic Impairment Constraint Network for Transparent Mesh Optical Networks
Period：2008.1～2010.7
Partners：ADVA(DE), Alcatel-Lucent (FR), ECI (IL), Huawei (DE), DTAG (DE), AIT (GR), Create-Net (IT), ENST (FR), IBBT (BE), RACTI (GR), UEssex (UK), UPC (ES) and JCP (FR)
Objective：The development of a dynamic network planning tool residing in the core network nodes that incorporates real-time measurements of optical layer performance into IA-RWA algorithms and is integrated into a unified control plane
One of project objectives - Protocol extensions to enable an Impairment Aware-control plane, which is related to IETF CCAMP scope

## Slide 4: Objective
Based on the result of “Protocol extensions to enable an Impairment Aware-control plane” in DICONET project
Define extensions to the OSPF routing protocol in support of impairment aware RWA in WSONs

## Slide 5: OSPF routing for IA-RWA -New PLI TLV
In GMPLS-based WSON networks, the following information need to be flooded through routing:
Normal routing info: described in [RFC 3630] and [RFC 4203].
  Node ID, Link ID, Administrative Group, ISCD, Protection, TE metric, …
RWA info: described in [rwa-info] , [rwa-encode] and [rwa-ospf]
  Switch Connectivity Matrix, Wavelength Converter Pool info, Wavelength Availability, Port Wavelength Restriction, ...
Impairment info: this draft involved
Two top-TLVs are defined to describe PLI (Physical Layer Impairments) information:
  Link PLI TLV -Describes the physical layer impairments related to the link
  Node PLI TLV -Describes the physical layer impairments related to the node

## Slide 6: The composition of Link PLI TLV
PLI LSA
TOP TLV (Link PLI TLV)
PLI LSA header
Link ID sub-TLV
Local interface IP sub-TLV
Remote interface IP sub-TLV
Component Impairment sub-TLV
Wavelength unrelated Impairment sub-sub-TLV
Wavelength related Impairment sub-sub-TLV
Wavelength Id
Parameter sub-sub-sub-TLV
Other component sub-TLV....
Other Parameter sub-sub-sub-TLVs...
Other Wavelength related Impairment
sub-sub-TLVs ...
Parameter sub-sub-sub-TLV
Other Parameter sub-sub-sub-TLVs…
Component ID
Component: The elements that the link passes through:
  0=Transmitter
  1= Fiber
  2= DCM
  3=Attenuator
  4=Receiver
  5=Amplifier

## Slide 7: The composition of Node PLI TLV
Component type:
  8=Physical node
PLI LSA
TOP TLV (Node PLI TLV, type=1)
PLI LSA header
Node IP sub-TLV
Component Impairment sub-TLV
Other component sub-TLV
......
Wavelength unrelated Impairment sub-sub-TLV
Wavelength related Impairment sub-sub-TLV
Wavelength ID
Parameter sub-sub-sub-TLV
Other Parameter sub-sub-sub-TLVs....
Other Wavelength_related Impairment
sub-sub-TLVs ......
Parameter sub-sub-sub-TLV
Other Parameter sub-sub-sub-TLVs...
Component ID

## Slide 8: Some sub-TLVs and sub-sub-TLVs
Component impairments sub-TLV Format
Impairment Parameter Sub-sub-sub-TLV Format
Wavelength related Impairment Sub-sub-TLV Format
Wavelength unrelated Impairment Sub-sub-TLV Format

## Slide 9: Parameter Types for the Link PLI TLV
Note that this table can be updated based on ITU-T definition related to physical impairments. The TLV format do not need to be changed when the physical impairments definition updated.
Component type | Parameter Type | Wavelength related?
0 = Transmitter | 1 = bitrate | Related
 | 2 = power | Related
 | 3 = Center wavelength (for each channel) | Related
 | … | 
1 = Fiber or 2 = DCM | 21 = fiber type | unrelated
 | 22 = fiber length | unrelated
 | 23 = Dispersion parameter (D) | Unrelated
 | 24 = Dispersion slope | 
 | … | 
3 = Attenuator | 61 = Attenuation (Attn) | related
4 = Receiver | 81 = Responsivity | related
 | 82 = Absolute threshold level | related
 | … | 
5 = Amplifier | 101 = Spontaneous emission factor (nsp) | unrelated
 | 102 = Amplifier Gain (GaindB) | unrelated
 | … | 

## Slide 10: Parameter Types for the Node PLI TLV
Note that this table can be updated based on ITU-T definition related to physical impairments. The TLV format do not need to be changed when the physical impairments definition updated.
Component type | Parameter Type | Wavelength related?
8 = Physical node | 161 = inner filter type | unrelated
 | 162 = inner filter order | unrelated
 | 163 = Noise equivalent bandwidth factor | unrelated
 | 164 = 3-dB bandwidth | related
 | 165 = center wavelength for each channel | related

## Slide 11: An Example of component TLV
Component Impairment sub-TLV (=1, fiber component)
Component ID sub-sub-TLV (ID = xx)
Wavelength_irrelated Impairment sub-sub-TLV
Parameter sub-sub-sub-TLV [(Type=21(fiber type), velue=1(SSMF)]
Parameter sub-sub-sub-TLV [ Type=22(fiber length), velue=10KM]
Wavelength_related Impairment sub-sub-TLV
Wavelength #1 (λ1)
Parameter sub-sub-sub-TLV [Type=23(D), velue=1.7e-5]
Parameter sub-sub-sub-TLV [Type=24(dD), velue=56.7]
Wavelength_related Impairment sub-sub-TLV
Wavelength #2 (λ2)
Parameter sub-sub-sub-TLV [Type=23(D), velue=1.8e-5]
Parameter sub-sub-sub-TLV [ Type=24(dD), velue=57.7]
Wavelength_related Impairment sub-sub-TLV
Wavelength #3 (λ3)
Parameter sub-sub-sub-TLV [Type=23(D), velue=1.9e-5]
Parameter sub-sub-sub-TLV [Type=24(dD), velue=58.7]
Wavelength_related Impairment sub-sub-TLV
Wavelength #4 (λ4)
Parameter sub-sub-sub-TLV [Type=23(D), velue=2.0e-5]
Parameter sub-sub-sub-TLV [Type=24(dD), velue=59.7]

## Slide 12: Next Steps
Refine it according to the feedback from the meeting or mailing list
Keep upgrading when ITU-T defined the standard impairment information
Comments are always appreciated
Notes: <number>