## Slide 1: Proposal for Tuning IGMPv3/MLDv2 Protocol Behavior in Wireless and Mobile networks
draft-wu-multimob-igmp-mld-tuning-02
Qin Wu
Hui Liu

## Slide 2: Status
Second Presentation in the Multimob
Changes since -01 (Presented in Anaheim)
  Remove Optimization Consideration for Report Messages
  Remove the optimization method for Limiting the scope of periodical Queries
  Highlight the explicit tracking feature
  Add Link model analysis for wireless multicast
  Comparison between wired multicast and wireless multicast
  Add Report Suppression Support
  Add Query Suppression Support

## Slide 3: Comparison between IGMPv2/MLDv1 and IGMPv3/MLDv2

## Slide 4: Comparison between wired multicast and wireless multicast

## Slide 5: Wireless Link Models Analysis

## Slide 6: Router behavior for tuning optimization
Explicit Tracking of hosts
Suppression Consideration
  Report Suppression for the hosts
  Query Suppression for the routers
Using Unicast Query
  Collecting membership by Using General Query with Unicast Query
  Switching Between Unicast Query and Multicast Query
Link Type Consideration
  Filtering unwanted multicast packets based on link type
  Tuning Response Delay according to link type and status
Minimizing General Periodical Query Frequency by increasing interval each time
Multiple Retransmission of Queries on packet loss

## Slide 7: Explicit Tracking of hosts
How to do explicit tracking
  The router may use local replication to inspect incoming join and leave requests,
  The router records or refreshes the membership state for each host on the interface,
  and the router take appropriate action to each received report.
  The router builds a table to track which channel being forwarded to each port
How to optimize explicit tracking
  Disable Group specific Query or Source-and-Group Specific Queries when explicit tracking is used.
  update membership state periodically by using periodical IGMP/MLD Query.
  Separation of processing state changing report and current state report

## Slide 8: Suppression Consideration(1)
Report Suppression for the hosts
  The router can terminate IGMP/MLD reports coming from hosts, and forwards a summarized version to the router/Querier.
  Unsolicited membership reports (channel change requests) are forwarded only the first subscriber joins a multicast group, or the last subscriber leaves a multicast group. This tells the upstream router to begin or stop sending this channel to this router.
  Solicited membership reports (sent in response to an query) are forwarded once per multicast group. The router may also aggregate multiple responses together into a single membership report.

## Slide 9: Suppression Consideration(2)
Query Suppression for the routers
  The downstream router stop forwarding IGMP/MLD Queries packets sent to the hosts and respond with report as proxy to the upstream router
    Never send a specific query to any client
    Send general queries only to those clients receiving at least one multicast group

## Slide 10: Link Type Consideration
Filtering unwanted multicast packets based on link type
  the multicast capability within a link may cause for a receiver to wake up for unwanted multicast packet
  Filtering the multicast packets and delivering the packets to only for receivers that are listening for particular multicast packets
  broadcast link model and point to multipoint link model require filtering at the access node to support the dormant mode for the receivers
Tuning Response Delay according to link type and status
  If the link type is PTP which means the resource is dedicated for one receiver on each link, then the Maximum Response Delay can be chosen smaller
  If the expected number of Reporters is small and the link condition is good, the administrator may choose the smaller Maximum response Delay

## Slide 11: Using Unicast Query
Collecting membership by Using General Query with Unicast Query
  Using General Query to collect most of the membership report response
  Using Unicast Query to collect the membership report again from each non respondent receiver.
Switching Between Unicast Query and Multicast Query
  switch between unicast and multicast Query based on the receiver numbers.

## Slide 12: Mailing List Discussion Summarization
IGMP/MLD proxying
  based on the aggregate state it sends messages upstream.
  send general queries downstream, independently of when the upstream sends them
Is Wireless link asymmetrical link
  wireless link for multicast is possible to be asymmetrical link
  possible for hosts to send multicast data on a wireless link
  possible to have one asymmetric link for wired network
Host reduce Power consumption by removing host suppression
  the host does not need to spend any processing power to listen and determine whether there are duplicated report message.
Using specific queries instead of general queries
  miss lots of solicited report which is early used to do membership state update and new group collection on the router
  if the router never received an unsolicited report from the host, then the router can only learn about that group if it sends a general query
  Remove this case
Explicit tracking is mandatory to IGMPv3/MLDv2
  Explicit tracking is allowed, but not mandatory

## Slide 13: Moving Forward
Adopt it as WG item?
Solicit more review and quick Feedback