## Slide 1: MultiMob WG. Potential future work (draft-von-hugo-multimob-future-work-02)
IETF 78, Maastricht / 2010-07-27
Dirk von Hugo (Deutsche Telekom), Hitoshi Asaeda (Keio University), Hui Deng (China Mobile), Pierrick Seïté (France Telecom – Orange),
Notes: 15/04/2009
[HA] Dirk is the first author. I changed the order.

## Slide 2: Overview
2010/07/27
MULTIMOB-future work-78.ppt
<number>
MultiMob base solution proposals
  mobile multicast for PMIPv6
    draft-ietf-multimob-pmipv6-base-solution
  IGMP/MLD tuning for mobility
    WG draft will be decided soon
  Without modification of both standard protocols
  No specific mobility actions nor implementations are required at mobile nodes and routers
No consideration of additional extensions to enhance performance such as
  Smooth (or fast) handover
  Conservation of network resources and routing/tunnel convergence
  Performance optimization
  Local routing
  Source mobility
  etc.
Notes: [HA] I changed
15/04/2009

## Slide 3: Possible future work in MultiMob WG
2010/07/27
MULTIMOB-future work-78.ppt
<number>
Enhancement of multimob base solution in terms of:
  PMIPv6 base solution modification
  PMIPv6 protocol modification
  IGMP/MLD protocol modification
Application of (existing) advanced protocol features (e.g. from MEXT, MIPSHOP, ...):
  Impact of mobility related connectivity changes (handover) to be minimized by adaptation of unicast traffic handling for multicast group management
Further deployment specific issues:
  dynamic and/or automatic tunnel configuration
  direct or local routing approach (AKA local break-out)
Long-term future extensions (?):
  source mobility
  support of multiple flows on multi-homed mobile nodes
  mobile multicast for multi-hop transmission
Notes: [HA] I changed.
15/04/2009

## Slide 4: Future work in MultiMob WG Enhancement of base multimob solution
2010/07/27
MULTIMOB-future work-78.ppt
<number>
MAG1
MN1
MAG2
LMA1
LMA2
Internet
PMIP6 domain
MC source
M-Tunnel
Hold/release or ack msg
Modification of PMIP6 operation:
  choose e.g. LMA1 to care especially for MultiCast only
  …
Extension of PMIPv6:
  Introduce specific MC tunnel (LMA-MAG or MR-MAG)
  Smooth handover
  …
Extension of IGMP/MLD:
  Add router control or acknowledgement messages
  …
DM-LMA
Notes: 15/04/2009

## Slide 5: Future work in MultiMob WG Adopt advance mobility features
2010/07/27
MULTIMOB-future work-78.ppt
<number>
Fast Handover for multicast traffic management:
  Multicast Context Transfer
  new messages to trigger transfer of new multicast information option.
  new mobility messages and options for extended HI and HAck
P-MAG
MN1
N-MAG
LMA1
LMA2
Internet
PMIP6 domain
MC source
Fwd Tunnel
Notes: 15/04/2009

## Slide 6: Future work in MultiMob WG Further deployment-specific issues: Direct or local routing
2010/07/27
MULTIMOB-future work-78.ppt
<number>
Automatic dynamic tunnel set up:
  connection of singular MC enabled routers (MBONED proposal)
Separation of mobility entity LMA and Multicast Router
MAG1
MN1
MAG2
LMA1
LMA2
Internet
PMIP6 domain
MC source
Notes: 15/04/2009

## Slide 7: Future work in MultiMob WG (Long-term) future extension: source mobility
2010/07/27
MULTIMOB-future work-78.ppt
<number>
source mobility:
  address transparency
  packet loss and multicast scoping
  decoupling between sender and receiver
LMA as Rendezvous Point (RP) for multicast join
MAG1
MN1
MAG2
LMA1
LMA2
Internet
PMIP6 domain
MC source
RP
Notes: 15/04/2009

## Slide 8: Future work in MultiMob WG (Long-term) future extension: support of multiple flows
2010/07/27
MULTIMOB-future work-78.ppt
<number>
support of multiple flows on multi-homed mobile nodes
  Adaptation of flow mobility support within WGs MEXT or NETEXT
MAG1
MAG2
LMA1
LMA2
Internet
PMIP6 domain
MN2
if1
if2
MC source2
MC source1
Notes: 15/04/2009

## Slide 9: Future work in MultiMob WG (Long-term) future extension: multi-hop scenario
2010/07/27
MULTIMOB-future work-78.ppt
<number>
mobile multicast for multi-hop transmission:
  e.g. wireless mesh and multiple NEMOs
Analogue to Simplified Multicast Forwarding for MANET?
MAG1
MAG2
LMA1
LMA2
Internet
PMIP6 domain
MN2
MC source
MR
MAG3
Notes: 15/04/2009

## Slide 10: Possible future work in MultiMob WG Available drafts (AFAWK)
2010/07/27
MULTIMOB-future work-78.ppt
<number>
Enhancement of multimob base solution in terms of:
  PMIPv6 base solution modification (draft-zuniga-multimob-smspmip)
  PMIPv6 protocol modification (draft-asaeda-multimob-pmip6-extension)
  IGMP/MLD protocol modification (draft-asaeda-multimob-igmp-mld-mobility-extensions, draft-liu-multimob-reliable-igmp-mld )
Application of (existing) advanced protocol features (e.g. from MEXT, MIPSHOP, ...):
  Impact of mobility related connectivity changes (draft-schmidt-multimob-fmipv6-pfmipv6-multicast, draft-contreras-multimob-rams, draft-hui-multimob-fast-handover-02)
Further deployment specific issues:
  dynamic and/or automatic tunnel configuration (draft-ietf-mboned-auto-multicast-10)
  direct or local routing approach (AKA local break-out) (draft-sijeon-multimob-mms-pmip6, draft-asaeda-multimob-pmip6-extension)
Long-term future extensions (?):
  source mobility (draft-zhang-multimob-msm)
  support of multiple flows on multi-homed mobile nodes (no drafts yet)
  mobile multicast for multi-hop transmission (no drafts yet)
Notes: [HA] I changed.
15/04/2009

## Slide 11: Thank you! Questions please …
Notes: 15/04/2009