## Slide 1: Problem Descriptions
Chairs
<number>
Notes: <number>

## Slide 2: Problems
One slide per problem proposed
First the proposer talks about it
Next WG comments are solicited
Chairs only to judge the consensus
<number>
Notes: <number>

## Slide 3: Protocol Extensions
draft-asaeda-multimob-igmp-mld-mobility-extensions-04.txt
Approaches
  For smooth handover: Host-side protocol extensions
    IGMP/MLD Notification operation
      MN explicitly notifies current-state report without solicitation (i.e. without waiting general query)
    IGMP/MLD Hold and Release operations
      MN asks to keep MN’s membership state to its upstream router during its handover, and release after its handover
  No interoperability problem exists
Notes: <number>

## Slide 4: How to Gain Reliability for IGMPv3/MLDv2 in Wireless and Mobile networks
<number>
Problem in Wireless and Mobile Networks
  IGMP/MLD is not a reliable protocol
  IGMP/MLD can not gain reliability by sending several copies of IGMP messages.
    Packet loss is very high when IP multicast works in a radio environment
    Unsolicited Report is prone to loss due to network conditions degradation or long
    distance travel, which will have bad effects on user’s experiences
    Even the report can be retransmitted for several times, the report reception by the
    router can not be guaranteed.
    And excessive packet retransmission is a waste of resource
  INTEL Wimax lab observes this issue as well in the lab test.
  This problem is discussed by IPMSI at the following URL link: http://www.ipmulticast.com/content/view/20/2/
Proposal in draft-liu-multimob-reliable-igmp-mld-00.txt
  Adopting acknowledgement-retransmission to improve the reliability
    A host after sending an unsolicited report starts a retransmission timer and waits for the acknowledgement (ACK) from the router.
    Upon receiving ACK or multicast data, the host stops the timer and retransmission.
    If the ACK not received when the timer expires, another report is retransmitted.
  Using new message and parameters
    ACK message is introduced, either using new message type or reusing report type message with flag set
    A retransmission timer and a retransmission counter are maintained by the host to control the process of retransmission
Notes: <number>

## Slide 5: 1. PMIP Direct Routing Option
Design optimized solution for the scenario of multicast services available throughout the access network independent of the PMIPv6 infrastructure
Jointly account for
  Flat access networks
  Tunnel- or VPN-based multicast feeds
  AMT-type scenarios
<number>
Notes: <number>

## Slide 6: Re-chartering proposal: Dedicated Multicast LMA
Basic concept being discussed in the group since last year (IETF76)
Advantages
  Not all LMAs need to support multicast capability and connectivity
    Reduces total resources and states at LMAs
    Reduces tunnel convergence issue at the MAG
    Minimizes the replication of multicast traffic when MNs with different LMAs join the same multicast group
  Simplifies the multicast tree topology
    Allows a PMIPv6 domain to closely follow a simple multicast tree topology for Proxy MLD forwarding
Related drafts
  https://datatracker.ietf.org/doc/draft-zuniga-multimob-smspmip
  http://tools.ietf.org/html/draft-contreras-multimob-msd-00
  https://datatracker.ietf.org/doc/draft-sijeon-multimob-mms-pmip6
<number>
Notes: <number>

## Slide 7: 3. Multicast Context Transfer Extensions of FMIPv6/PFMIPv6/…
Define a generic context transfer scheme for multicast state records that works for FMIPv6, PFMIPv6 and comparable protocols
Initial proposal:
draft-schmidt-multimob-fmipv6-pfmipv6-multicast
<number>
Notes: <number>

## Slide 8: Protocol Extensions
Supported Functions
  Set up a bi-directional tunnel link (M-Tunnel) between LMA and MAG for traffic aggregation
    M-tunnel is dedicated to multicast data and message transmission between LMA and MAG
  Support smooth handover by PBU with multicast extension (PBU-M) message
    Compliant with M-CTD with CXTP or Policy Profile
  Provide flexibility for various use cases (scenarios) and combinations of functions
    Either “Routing function (PIM-SM)” or “Proxy function (MLD proxy)”, or dual-mode (i.e. support both functions)
  Support local routing (when MAG acts as a PIM router)
Notes: <number>

## Slide 9: Fast Handover
It is proposed to add fast handover issue into Multimob charter
  Without supporting fast handover, it will cause packet loss
    In multimob, only after the bi-directional tunnel is built between n-MAG and, the multicast packet can be continuously delivered to MN. It inevitably causes the latency and loss of packet during handover process.
  Fast handover has been considered in other mobility issues
    Fast handover is an important item in Mobile IPv6 specified RFC5268
    draft-irtf-mipshop-pfmipv6 extends the FMIPv6 and applies it to the PMIPv6
Fast handover has been talked a lot in Multimob mail list, and there are two related drafts:
  draft-hui-multimob-fast-handover
  draft-schmidt-multimob-fmipv6-pfmipv6-multicast
<number>
Notes: <number>

## Slide 10: Protocol extension to accelerate the MAG’s knowledge of the MN’s multicast subscription after HO
MAG entity in base solution relays on standard MLD procedures to get knowledge of MN multicast subscription after handover
Several delay sources contribute to increase the timing for multicast delivery at the new point of attachment
  Delay due to the access to radio resources among competing MNs
  Delay due to radio frame structure
  Delay due to retransmissions caused by radio channel unreliability
  Delay due to MLD message processing at MN
Item proposal: to accelerate the MAG’s knowledge acquisition of the MN’s multicast subscription by means of new signaling messages internal to the network, decoupling subscription acquisition from
  Underlaying radio technology
  IGMP/MLD parametrisation tuning
  PMIPv6 multicast architecture (current or evolved)
Intended draft: draft-contreras-multimob-rams-00
<number>
Notes: <number>

## Slide 11: 2. PMIP Multicast Source Support
Develop a solution that smoothly extends sender support from the base-solution to optimized direct routing
<number>
Notes: <number>

## Slide 12: draft-zhang-multimob-msm-00.txt
Scenarios
Protocol
“S” flag denotes that MN is a multicast source.
“J” flag denotes which scheme is used.
J=1，SPT-based scheme; J=0，RPT-based scheme.
Motivation
The PMIPv6 MN may be a multicast source.
LMA which is a fixed node for MN can act as RP.
SPT can also be refreshed in a network- based manner.
Notes: Author: G. Arheilger, Juniper Networks, EMEA Central
Copyright © 2001 Juniper Networks, Inc. All rights reserved.
<number>

## Slide 13: Conclusions
Continue to discuss on the list
Possibility of having an online questionnaire
RFC 2418 describes revising milestones and rechartering procedures
<number>
Notes: <number>