## Slide 1: Multicast Source Mobility Support in PMIPv6 Network
draft-zhang-multimob-msm-01
Beijing Jiaotong University Tsinghua University
2010.11.9

## Slide 2: Outline
Motivation
Considerations for RPT and SPT
Solution and Procedure
Format of signaling messages

## Slide 3: Motivation
RFC 5757: the MN may be a multicast source.
Application Scenario: transportation vision distribution service based on the ITS (Intelligent Transport Systems) service.

## Slide 4: Considerations for RPT and SPT
RPT-based scheme: LMA which is a fixed node for MN can act as RP.
  Stable and unoptimized multicast tree
SPT-based scheme: Reconstruct the multicast tree once the L3 network layer) handover happens.
  Unstable and optimized multicast tree

## Slide 5: Considerations for RPT and SPT
Deficiencies of the SPT-based scheme
  No big differences between the two paths.
  The unstability of the multicast tree
  Providing address transparency at two layers is a tough problem for the SPT-based scheme.
Choose the RPT-based scheme

## Slide 6: Solution and Procedure

## Slide 7: Format of signaling messages (1/3)
PBU
  0 1 2 3
  0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  | Sequence # |
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  |A|H|L|K|M|R|P|S| Reserved | Lifetime |
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  | |
  . .
  . Multicast address option .
  . .
  | |
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  S flag: identify whether the MN is a multicast source or not.
  Multicast address option: the related multicast address

## Slide 8: Format of signaling messages(2/3)
PBA
  0 1 2 3
  0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  | Status |K|R|P|S| Res. |
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  | Sequence # | Lifetime |
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  | |
  . .
  . Multicast address option .
  . .
  | |
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  S flag and Multicast address option: the S flag is set to "1" if the LMA can act as the RP for the multicast service identified by the Multicast address option.

## Slide 9: Format of signaling messages(3/3)
Multicast address option
  0 1 2 3
  0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  | Option Type | Option Length |
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  | |
  + Multicast address +
  | |
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  Option Type: TBD
  Option Length: 8-bit unsigned integer indicating the length of the option in octets.
  Multicast address: The multicast address related to the multicast session provided by the MN.

## Slide 10
Thank you!