## Slide 1: Juan Carlos Zúñiga Akbar Rahman Luis M. Contreras Carlos J. Bernardos Ignacio Soto IETF 79, November 2010
Dedicated
Multicast LMA

## Slide 2: Dedicated Multicast LMA (1/2)
Joint draft = draft-zuniga + draft-contreras-msd
  Basic concept discussed since IETF 76 (Hiroshima)
All concepts and comments addressed now in this draft
  https://datatracker.ietf.org/doc/draft-zuniga-multimob-smspmip/
Scope of Changes:
  New sections on deployment scenarios
  Multicast LMA definitions and terminology updated
  PMIP enhancements:
    Binding Update
    Policy Profile
    MAG to LMA attach requirements

## Slide 3: Dedicated Multicast LMA (2/2)
Advantages
  Not all LMAs need to support multicast capability and connectivity
    Reduces total resources and states at LMAs
    Reduces tunnel convergence issue at the MAG
    Minimizes the replication of multicast traffic when MNs with different LMAs join the same multicast group
  Simplifies the multicast tree topology
    allows a PMIPv6 domain to closely follow a simple multicast tree topology for Proxy MLD forwarding
  Allows the implementation of a single MLD proxy instance per MAG to support the multicast service
    Reduces the complexity of the MAG
  Permits different PMIPv6 deployment scenarios
    Deployment strategies can be tailored for expected traffic scenarios

## Slide 4: Several unicast PMIPv6 domains served by one Multicast LMA (relationship N:1)
Suited for / Potential benefits:
Initial scenario for network deployment (scalable approach)
Reduced multicast tree size in core network and/or centralized content distribution
Adapted to low multicast-MN customer base (multicast equipment synergy, shared for high number of customers)
U-LMA
U-LMA
M-LMA
MAG1
MAG2
MAG3
MAG4
MAG5
Unicast
area
Unicast
area
Multicast
area
Unicast flow
Multicast flow
Multicast tree

## Slide 5: One unicast PMIPv6 domain served by several Multicast LMAs (relationship 1:N)
M-LMA
M-LMA
U-LMA
MAG1
MAG2
MAG3
MAG4
MAG5
Multicast
area
Multicast
area
Unicast
area
Unicast flow
Multicast flow
Suited for / Potential benefits:
Service differentiation: distinct content providers, transport technology (IPv4/v6), content type (premium vs non-premium), etc
Load balance, redundancy
Topological efficiency (best route to content source) [only if MAG implements multicast router capabilities]
Adaptability to multicast tree dynamics in core network
(very) High multicast MN customer base [no overlapping areas]
MLD proxy
Instance #2
MLD proxy
Instance #1
Multicast tree
Multicast tree

## Slide 6: Several unicast PMIPv6 domains served by one Multicast LMA (relationship N:1) with Hybrid LMA
Hybrid LMA
U-LMA
MAG1
MAG2
MAG3
MAG4
MAG5
Unicast
area
Unicast
area
Multicast
area
Unicast flow
Multicast flow
Multicast tree

## Slide 7
THANK YOU