## Slide 1: Proposal for Tuning IGMPv3/MLDv2 Protocol Behavior in Wireless and Mobile networks
Qin Wu Hui Liu
79th IETF Beijing
draft-wu-multimob-igmp-mld-tuning-03

## Slide 2: Contents
Outline
Proposed tuning options
Changes from ver-02
Comments on mail list
Future Direction

## Slide 3: Outline
Optimize IGMP and MLD to be applicable to wireless or mobile networks
Improve efficiency to reduce unnecessary packet transmission and robustness to prevent loss
Limit the changes within the protocol framework without introducing interoperability issues
Possibly extended to wired network where efficiency and robustness are required

## Slide 4: Proposed tuning options
Explicit Tracking and Query suppression
Minimizing Query Frequency by increasing interval
Switching Between Unicast and multicast Query
Using General Query with Unicast Query
Retransmission of General Queries
General Query suppression without receiver
Tuning Response Delay according to link type/status
Triggering Reports and Query quickly during handover

## Slide 5: Changes from ver-02
Augment two optimization options
o General Query suppression without receiver
o Triggering Reports and Queries quickly during
handover
Explain scenarios, requirements and solutions more clearly and concisely
Other editorial revisions

## Slide 6: General Query suppression without receiver
General Query is unnecessary if there is no valid receiver on a link
Should be suppressed in following cases:
o When using explicit tracking, if last number leaves the group, by checking membership database decides there is no valid receiver
o When not using explicit tracking, if last number leaves the group, after sending Group Specific or Source-and Group specific Query decides there is no valid receiver
o If after retransmission of General Queries on startup, fails to get any response;
o If previously has valid members, but fails to get any response after several rounds of General Queries or Unicast Queries;
Benefits: Avoid unnecessary consumption of link resources and terminal power

## Slide 7: Triggering Reports and Queries during handover
During handover, new access network should deliver the content to the receiver as soon as possible without introducing disruption or performance deterioration.
Terminal’s membership should be acquired as quickly as possible by new access network.
Access router should trigger a Query (General Query or Unicast Query) as it detects a new terminal on its link.
When in multicast reception state, terminal should trigger a Report as it detects connection to a new access network

## Slide 8: Comments on mail list
Shorten comparison of different versions of IGMP and MLD (Dirk)
Emphasize the characteristics of wireless asymmetrical link (Dirk)
Explain the reason why explicit tracking benefits fast channel zapping (Dirk)
Explain whether tuning timer according to link status and/or type requires protocol change or not (Dirk)
Move detailed description of scenario to req. draft.
(Hitoshi)

## Slide 9: Future Direction
Thanks!
Adopted as a Working Group Document?