## Slide 1: Tuning the Behavior of IGMP and MLD for Mobile Hosts and Routers
draft‐asaeda‐multimob‐igmp‐mld‐optimization‐04a
Hitoshi Asaeda, Yogo Uchida
Keio University
79th IETF, November 2010, Beijing, China
<number>
Notes: <number>

## Slide 2: Outline
Enabling the explicit membership tracking function is SHOULD
Potential tuning values are proposed according to our experimental result
  Query Interval, Query Response Interval, Startup Query Interval
    Unicast Query Interval and Unicast Query Response Interval
  Robustness Variable
  Last Member Query Count (LMQC) / Last Listener Query Count (LLQC)
Please check the new draft;
  http://www.sfc.wide.ad.jp/~asaeda/paper/draft-asaeda-multimob-igmp-mld-optimization-04a.txt
<number>

## Slide 3: Simulation Scenario – WiFi
IEEE802.11b
IPv6 only
50 MNs randomly
join/leave the same
IPv6 multicast stream
(15 min, 320kbps)
One competitive
unicast stream
(10Mbps)
MNs moves with random waypoint algorithm
<number>

## Slide 4: Transit Number of Members – WiFi
<number>

## Slide 5: Tracking of Membership State
“IGMP/MLD-Based Explicit Membership Tracking Function for Multicast Routers”
  draft-asaeda-mboned-explicit-tracking-01
Contribution
  Enable per-host accounting
  Enable unicast general query that may minimizes the network resource consumption
  Reduce the number of Group(-and-Source) Specific query messages and its reply messages
  Shorten the leave latency by shorter LMQT/LLQT
  (Future extension) Enable intelligent query timer tuning based on the number of receivers.
The explicit tracking function is SHOULD for multicast routers (or proxies) maintaining mobile nodes
<number>
Notes: <number>

## Slide 6: Current-State Report – Regular Case
Responses for General Queries (125)
Responses for Group- (and-Source) Specific Queries
<number>

## Slide 7: Current-State Report – Explicit Tracking
Responses for General Queries (125)
Responses for ONE Group- (and-Source) Specific Query
<number>

## Slide 8: Tuning Strategy – 1
Query Interval (125) and Query Response Interval (10)
  If short,
    Quick membership record synchronization
  If long,
    Less link congestion
  How balance?
    For resource sensitive link, the default value (125) or a bit longer value (150) may be adopted
    For not resource sensitive link, shorter Query Interval (e.g. 60 to 90) and shorter Query Resp. Int. (e.g. 5) can be adopted
<number>

## Slide 9: Tuning Strategy – 2
Unicast Query Interval and Unicast Query Response Interval
  If used,
    No drain on battery power for non-member nodes
  It does not eliminate the regular multicast General Query (in order to discover nodes whose unsolicited report are missed)
  It should be shorter than the regular (i.e. multicast) Query Interval
Note
  RFC3376 and 3810 do not distinguish multicast and unicast General Query and do not define different timer values
  Protocol extension?
<number>

## Slide 10: Tuning Strategy – 3
Robustness Variable (2)
  If big,
    Robust, because possibility of loosing unsolicited reports messages decreased
  If small,
    Possibility increased
      But the explicit tracking will give correct sense about last member
  How balance?
    The default value (2) may be adopted in the regular cases
    The small value, “1”, can be adopted when shorter Query Interval (e.g. 60 to 90) and shorter Query Resp. Int. (e.g. 5) are adopted for a router enabling explicit tracking recover (because the condition in which a router misses unsolicited messages will be recovered by General Query in the shorter period)
<number>

## Slide 11: Tuning Strategy – 4
LMQC / LLQC (Robustness Variable times)
  LMQT (=LMQC*LMQI (1)) / LLQT are sensitive factors
  If small,
    Shortening leave latency
  If big,
    Robust from packet loss
  How balance?
    Use the default value (Robustness Variable times)
      Hence LMQT/LLQT = 2 seconds
    Configuration being Robustness Variable = “1” will shortening the leave latency, as well
<number>

## Slide 12: Tuning Strategy – 5
Startup Query Interval (1/4 of [Query Interval] (e.g. 25 sec.))
  If short,
    Quick new member discovery
  If long,
    No strong benefit?
  How balance?
    1 second
<number>

## Slide 13: Simulation Scenario – WiMAX
IEEE802.16e
  20MHz (approx.
  21Mbps)
IPv6 only
100 MNs randomly
join/leave the same
multicast stream
(15 min, 3.2Mbps)
One competitive
unicast stream
(10Mbps)
MNs moves with
random waypoint algorithm
<number>

## Slide 14: Transit Number of Members – WiMAX
<number>

## Slide 15: Tuning “Example”
<number>
Notes: <number>

## Slide 16: Next Step
Improve the quality of strategies based on more complex simulation scenarios
WG document ?
Also need IGMPv3/MLDv2 extension?
  Intended status is Experimental?
<number>
Notes: <number>
<number>