## Slide 1: Multicast Listener Extensions for MIPv6 and PMIPv6 Fast Handovers draft-schmidt-multimob-fmipv6-pfmipv6-multicast-03
Thomas C. Schmidt
t.schmidt@ieee.org
HAW Hamburg

## Slide 2: Status of the Draft
First introduced in Anaheim (IETF 77) (v1)
Defines a generic context transfer scheme for multicast state records that works for FMIPv6, PFMIPv6 and similar protocols
Update Version 2 (Sept.):
  Major revision, filled in details
Update Version 3 (Nov.):
  Filled in remaining details

## Slide 3: Main Contributions
Defines a coherent multicast membership transfer based on MLD/IGMP state records (easy handling)
Defines a common Multicast Mobility Header Option
Defines per group feedback in Multicast Acknowledgement Option
Dynamically steers Multicast forwarding via MLD
Accounts for MLD/IGMP interoperability
Seamlessly plugs into FMIPv6 and PFMIPv6 protocol semantics and behavior

## Slide 4: Core Operations
Detect / anticipate movement as in (P)FMIPv6
Construct Mobility Header Multicast Option and exchange in (FBU)-HI
Acknowledge in Mobility Header Multicast Acknowledgement Option and return unsupported groups in HACK-(FBACK)
Asynchronously join groups in new access network using loopback (NAR/NMAG)
Organize a per group (channel) forwarding between ARs by MLD (proxy-like approach)
On re-attachment of the MN, AR starts forwarding

## Slide 5: New Multicast Mobility Option
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Length | Option-Code | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
+ +
| |
+ MLD (IGMP) Report Payload +
~ ~
~ ~
| |
+ +
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Option-Code:
1: IGMPv3 Payload Type
2: MLDv2 Payload Type
3: IGMPv3 Payload Type from IGMPv2 Compatibility Mode
4: MLDv2 Payload Type from MLDv1 Compatibility Mode

## Slide 6: New Multicast Acknowledgement Option
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Length | Option-Code | Status |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
+ +
| |
+ MLD (IGMP) Unsupported Report Payload +
~ ~
~ ~
| |
+ +
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Option-Code: 0
Status:
1: Report Payload type unsupported
2: Requested group service unsupported
3: Requested group service administratively prohibited

## Slide 7: MLD/IGMP Compatibility Aspects
ARs need to support MLDv2/IGMPv3 (problem with host suppression)
According to MLD/IGMP specs: Compatibility mode required – can use MLDv1/IGMPv2
Routers translate into MLDv2/IGMPv3 equivalents and report on status in option code

## Slide 8: Summary & Outcome
Protocol defined incl. details
Initial reviews arrived:
  Please have a look & help to improve the document!
Proposal to WG:
Anticipate this as a WG item in future charter

## Slide 9
Questions/Comments?