## Slide 1: IPv6 in 3GPP Evolved Packet System
IETF#80 V6OPS WG, 31-March-2011
draft-korhonen-v6ops-3gpp-eps-06
J. Korhonen, J. Soininen, B. Patil, T. Savolainen, G. Bajko, K. Iisakkila

## Slide 2: Outline
History & Timeline
Updates since IETF#79
  Operational aspects of IPv6-only
  IPv6 Address configuration clarifications
  IPv6 Roaming considerations
  Inter-RAT handovers and fallback scenarios
Next Steps

## Slide 3: History & Timeline
First presented in IETF-3GPP workshop in SFO just before IETF#74; to document how IPv6 fits into 3GPP EPC..
Presentations in IETF#77 and #79.
Since then (-00) the draft has evolved to cover important parts of IPv6 from pre-Rel-8 (GPRS), Rel-8, Rel-9 and some Rel-10.

## Slide 4: Updates since IETF#79
Made the draft “opinion neutral”
  Only documents what is specified by 3GPP.
Operational aspects of IPv6-only networks
  Basic gotchas documented from 3GPP PoV.
  Removed some pros associated with dual-stack approach.
  IPv6 Address configuration clarifications
    About /64 uniqueness,
    GGSN/PGW generated IID, and
    Handling of PIOs.

## Slide 5: Updates since IETF#79 cont’d
  IPv6 Roaming considerations:
  There is motivation to restrict IPv6 roaming when it does not officially exist or the service quality cannot be guaranteed..
  Discuss ways to enable / prohibit roaming in case by case granularity.. currently no standardized method available.
Inter-RAT handovers and fallback scenarios:
  There are IPv4, IPv6 and IPv4v6 PDN Types to select from.
  There are IPv4, IPv6, IPv4v6 and IPv4_or_IPv6 in provisioning
  Which type to select depends on settings in UE, MME, HSS/HLR and GGSN/PGW.. not to forget legacy SGSNs that may modify requested types in between.
  UE may receive an indication whether opening two bearers to mimic IPv4v6 is ok or not if requesting IPv4v6 fails etc.

## Slide 6: Possible additional content considerations..
The draft is ~ready content/topic wise, however:
  One could add some text related to RFC3316 recommendations, although the RFC is not about EPC.
  Also a reference to RFC3314, although the RFC is not about EPC.

## Slide 7: Question to v6ops WG
Adopt this I-D as v6ops WG doc?
  Can proceed to WGLC immediately since content is fairly complete