## Slide 1: Accelerated Routing Convergence for BGP Graceful Restart
draft-keyur-idr-enhanced-gr-00
Keyur Patel, Enke Chen, Rex Fernando, John Scudder
IETF 81, July 2011, Quebec City, Canada
Notes: 1

## Slide 2: Motivation
Full Table re-announcements and cleanups across session resets are becoming expensive in BGP
  Newer AFs added to BGP adds to number of tables that BGP stores and announces
  BGP AF table size is growing as well. VPN AF table sizes already in excess of 1.4M routes
Would like to perform incremental updates within BGP to speed up convergence

## Slide 3: Advantages of Incremental Table Exchanges
Avoid table/prefix cleanups upon session resets
  Stale path timer cleans up table/routes if session does NOT come up within *restart* time period
Avoid exchanging Full BGP tables upon successive session restarts
  Results in faster Convergence
Highly beneficial in terms of CPU and transient memory usage

## Slide 4: Requirements for BGP Incremental Updates
Need to preserve ADJ-RIB-IN and ADJ-RIB-OUT during session resets
Need an ability to exchange incremental updates – Aka versioning of prefixes and routing updates
Need to signal if outbound and inbound RIBs have been preserved during the session reset or not
  Crucial in generation of incremental updates
Seems like a natural extension to an existing BGP Graceful Restart mechanism

## Slide 5: Enhanced GR aka Incremental updates
Augmented BGP GR to support Incremental route updates
Reuse GR to preserve
  BGP ADJ-RIB-IN and BGP ADJ-RIB-OUT during BGP session resets
Introduced new BGP GR Capability AF Flags
  (R) Flag used to indicate if the received routing state of ADJ-RIB-IN has been preserved or not
  (T) Flag used to indicate if the send routing state of ADJ-RIB-OUT has been preserved or not

## Slide 6: Enhanced GR
Introduced a new BGP Capability known as Enhanced GR Capability
  Used to indicate the support for a newly defined BGP Update Version message
  Used to indicate support for new AF level GR Capability flags
Introduced a new BGP message known as a BGP Update Version message
  Has a message subtype indicating if the message is a 1) send version number message, 2) Ack version number message, 3) Req version number message
  8 byte Version number

## Slide 7: Enhanced GR Operation
Enhanced GR Capability needs to be exchanged for enabling Incremental Updates
Every BGP speaker uses version number (per AF per peer) to track
  routing updates and other states announced
  routing updates and other states received
Received version number is an opaque value from receiving BGP speaker’s perspective

## Slide 8: Enhanced GR Operation
BGP speakers supporting Enhanced GR needs to exchange Update version messages
  Send version messages (subtype = 1) after batch of update messages
  Ack version messages (subtype = 2) for every version message with (subtype = 1) received
  Optionally request a peer to send update message from a certain version number (subtype = 3)
Upon session restarts BGP speakers explicitly exchange their ADJ-RIB-IN and ADJ-RIB-OUT state since the session reset
  If ADJ-RIB-OUT is not preserved then full table needs to be announced. Otherwise incremental updates are good enough
  If ADJ-RIB-IN is not preserved then full table is requested. Otherwise incremental updates are good enough

## Slide 9: Current GR Scenario for Session Restart
OPEN, Adjacency Up
BGP Peer
BGP Peer
Session disconnects, Marks prefixes as stale Mark prefixes as stale, start restart timer
Starts the restart timer
Send complete table updates, EOR
Send complete table updates, EoR
Stop restart timer. Start stalepath timer Stop the restart timer. Start stale path timer
Stop stalepath timer. Delete stale prefixes Stop stalepath timer. Delete stale prefixes if needed needed

## Slide 10: Enhanced GR Scenario for Session Restart
OPEN, Adjacency Up
BGP Peer
BGP Peer
Session disconnects, Start the restart timer Start the restart timer
Send incremental updates, Update Version message (subtype = 1)
Send incremental updates,
Update Version message (subtype =1)
No further action for Incremental mode No further action for Incremental mode
Checkpoint received version number
Checkpoint received version number
Send Update Version message ack (subtype =2)
Send Update Version message ack (subtype =2)

## Slide 11: Questions?