## Slide 1: PMIPv6 Extension for Multicast draft-asaeda-multimob-pmip6-extension-06
Hitoshi Asaeda
Pierrick Seite
Jinwei Xia
81st IETF, July 2011, Quebec City, Canada

## Slide 2: Protocol Extensions
Multicast traffic aggregation
  Set up bi-directional GRE tunnel (M-Tunnel) between LMA and MAG
    M-tunnels are dedicated to multicast data and message transmission between LMA and MAG and shared by all MNs at the MAG
Mobility support (i.e. seamless handover)
  Scenario 1: With Policy Profile
    When MN’s subscribing channel list is always maintained
  Scenario 2: With multicast extended PBU/PBA
    Use DeReg PBU and PBA having multicast channel information (PBU-M/PBA-M)
  Scenario 3: With other fast handover mechanism, e.g., multicast extended CXTP
    draft-vonhugo-multimob-cxtp-extension-00

## Slide 3: Background
Both LMA and MAG act as PIM-SM routers
  Support both ASM and SSM
Incoming IF on LMA/MAG is selected by an RPF lookup algorithm given by PIM
  No tunnel convergence problem
  Support local routing
  Friendly with source mobility
No multicast protocol changes
Notes: We assume PIM-SM, because PIM-SM is the most deployed multicast routing protocol.

## Slide 4: Changes from -05
Simplify the scenario
  No use case for MLD proxy
  Split CXTP extension into Dirk’s draft
    Instead, DeReg PBU is extended to notify subscribing multicast channel information
Adopt GRE for M-Tunnel
  Distinguish unicast transmission over IPv6-IPv6 LMA-MAG tunnel (according to Sri’s comment)
  GRE key is negotiated with RFC5845 or statically
Editorial changes

## Slide 5: Multicast Packet Format in M-tunnel
IPv6 header (src= LMAA, dst= Proxy-CoA) /* Outer Header */
GRE header /* Encapsulation Header */
IPv6 header (src= S, dst= G) /* Inner Header */
Upper layer protocols /* Packet Content */

## Slide 6: Conclusion
This draft provides the extension for PMIPv6 with PIM-SM
The way to move forward
  Go ahead with this story?
  Split into two drafts?
    “PMIPv6 multicast support with PIM-SM and M-Tunnel”
      Intended status: Informational or BCP or Proposed Standard
    “(P)BU/(P)BA extension for multicast handover”
      Intended status: Proposed Standard
6
81st IETF, July 2011