## Slide 1: Multicast Source Mobility Support in PMIPv6 Network draft-zhang-multimob-msm-03
Beijing Jiaotong University Tsinghua University
2011.7.25

## Slide 2: Outline
■ Problem Statement
  ◆Could the MAG support multicast communication?
  SolutionⅠ Extension for PMIPv6
  SolutionⅡ Multi-Upstream Interfaces MLD Proxy
  ◆ Could the LMA act as the DR?

## Slide 3: Could the MAG support multicast?
The MAG couldn’t forward multicast data from
the MN that acts as a multicast source for the
absence of the MFIB. For this, two
solutions are presented.
MAG
LMA
MN(source)

## Slide 4: Solution Ⅰ
MAG
Adding the
corresponding
MFIB for the MN
MN MAG LMA
1) |--- Rtr Sol-------->| |
| |------- PBU ----->|
| | |
2) | (Multicast address option)
| | Accept PBU
| | (Allocate HNP,
| | setup BCE and Tunnel)
| |<------ PBA ------|
| | (HNP, Group) |
| | |
3) | Accept PBA |
| (Set Up Tunnel |
| and Routing, Update MFC) |
|<---- Rtr Adv ------| |
| | |
4） |-- Multicast Data-->|=Multicast Data==>|
LMA
MN(source)
Notes: Add the corresponding MFIB at the MAG so that multicast data originated from the MN could be sent transparently to the corresponding LMA.

## Slide 5
LMA
MAG
MLD Proxy
MN(source)
U-IFs
D-IFs
Disadvantages of multiple parallel MLD Proxy
functions running on one MAG:
1. Difficult for management and implementation
2. Route optimization issue
Solution Ⅱ
Notes: For each LMA, there will be a separate instance of a MLD proxy, thus, there are multiple MLD Proxy functions running at one MAG, which leads to some disadvantages.

## Slide 6
MAG
MUIMP
Multi-Upstream Interfaces MLD Proxy(MUIMP)
Advantages:
1. Easily to deploy, implement and manage
2. Avoid route optimization issue
Solution Ⅱ
LMA
MN(source)
U-IFs
D-IFs
Notes: Instead of it, only one MLD Proxy function with multiple upstream interfaces is required, which is called Multi-Upstream Interface MLD Proxy(MUIMP).
In this way, multicast data sent by the mobile source will be sent to:
1.Directly mobile receivers co-located at the same MAG
2.The corresponding LMA of the MN through the tunnel

## Slide 7
MN1 MN2 MAG(MUIMP) LMA1 LMA2
| | | | |
MN1 Attached | | | |
| | | | |
| MN2 Attached | | |
| | | | |
|After configuration of PMIP for MNs, the MUIMP | | |
| adds the corresponding tunnel interface as a | | |
| new upstream interface for each MN | | |
| | | | |
|--------------- Multicast Data --------------> | | |
| | |==Mcast Data==>| |
| | | | |
| |--- Multicast Data --->| | |
| | |==========Mcast Data=========>|
| | | | |
| | | | |
Solution Ⅱ

## Slide 8: Could the LMA act as the DR?
As described in RFC4601, the check of direct
connection might be failed, which might lead to the
LMA unable to conduct the DR function for the MN.
If the LMA could act as the DR:
ASM: source registration
SSM: forward multicast data according to the MFIB
If not:
Some extensions on the LMA should be needed
MAG
LMA
MN
(source)
Notes: As described in RFC4601, on receipt of data from S to G on interface iif, the DR will check:
Whether the source is directly connected
2. The iif is identical to the RPF interface
However, because the network prefix of the LMA’s interfaces is not the same with the HNP allocated to the mobile source, the check of direct connection will be failed, which leads to the LMA unable to conduct the DR function for the MN.
Therefore, some extensions on the LMA should be needed, which will be our future work for the
multicast source mobility in PMIPv6.

## Slide 9
Q & A
Thank You!