## Slide 1: Rapid acquisition of the MN multicast subscription after handover
Luis M. Contreras, Carlos J. Bernardos
Universidad Carlos III de Madrid (UC3M)
Ignacio Soto
Universidad Politécnica de Madrid (UPM)
Quebec City, MULTIMOB WG, July 2011
1

## Slide 2: Proposal Status
81st IETF, Quebec City
Initial draft version submitted for 78th IETF meeting in Maastricht
Proposal included in re-chartering discussion during 78th IETF
Draft firstly presented in Beijing 79th IETF meeting
Updated version submitted for 81st IETF:
draft-contreras-multimob-rams-01.txt
Currently waiting for feedback from the list to progress
2

## Slide 3: Draft Motivation
81st IETF, Quebec City
The draft covers the MULTIMOB charter goal of optimizing multicast traffic during a handover
Main contribution:
  to accelerate the MAG’s knowledge acquisition of the MN’s multicast subscription
    (i.e., IP addresses of the multicast group subscribed by the MN, and the source providing it)
Main advantages:
  MAG acquisition of MN’s multicast status is decoupled from:
    Underlaying radio technology: different delays for distinct technologies (framing, retransmissions, resource mgmt, etc)
    IGMP/MLD parametrization tuning: different delays due to MLD message processing capabilities by distinct MNs, different timers per IGMP/MLD distinct flavours (including those being defined in MULTIMOB)
    PMIPv6 multicast architecture (current or evolved): solution compatible with base solution and also with solutions being proposed for solving tunnel convergence issue
3

## Slide 4: Predictive handover
81st IETF, Quebec City
4

## Slide 5
81st IETF, Quebec City
5
Reactive handover