## Slide 1: Use of OSPF-MDR in Single-Hop Broadcast Networks draft-ogier-ospf-manet-single-hop-00
Richard Ogier
Presented by Tom Henderson
July 28, 2011

## Slide 2: Problem Statement and Background
There is a need to support single-hop broadcast networks in which different costs are associated with different neighbors on the same interface.
  One example is when the underlying radio system performs layer-2 routing, but has a different number of (layer-2) hops to (layer-3) neighbors.
The point-to-multipoint interface uses a point-to-point (Type 1) link to describe each fully adjacent neighbor, but is not scalable since every neighbor must become fully adjacent.
The OSPF-MANET extensions already solve this problem, since a single-hop broadcast network is a special case of a MANET.
Another solution for solving this problem is proposed in draft-nsheth-ospf-hybrid-bcast-and-p2mp-01.

## Slide 3: Summary of Presentation
OSPF-MDR (RFC 5614) extends OSPF to support MANET interfaces in a scalable manner, and therefore provides an efficient solution for single-hop broadcast networks without any modification.
A few optional simplifications are possible in single-hop networks:
  Simplified procedure for originating router-LSA that avoids checking whether a neighbor is routable.
  Simplified MDR selection algorithm, which is similar to the DR election algorithm of OSPF.
With the above simplifications and recommended configuration, OSPF-MDR provides a solution similar to draft-nsheth-ospf-hybrid-bcast-and-p2mp-01.

## Slide 4: OSPF-MDR Approach
OSPF uses the Designated Router (DR) and Backup DR to achieve scalability in broadcast networks, by requiring each non-DR/BDR router to form only two adjacencies (with the DR and BDR).
OSPF-MDR generalizes the DR and BDR to multihop wireless networks:
  The DR is generalized by selecting a small subset of routers, called MANET Designated Routers (MDRs) that form a connected dominating set (CDS).
  Backup MDRs (BMDRs) are also selected so that the MDRs and BMDRs together form a biconnected dominating set.
MDRs achieve scalability in MANETs similar to the way DRs achieve scalability in broadcast networks:
  MDRs have primary responsibility for flooding LSAs. Backup MDRs provide backup flooding when MDRs fail.
  Adjacency reduction may be used, in which adjacencies are formed only between MDR/BMDR routers and their neighbors.

## Slide 5: Basic Idea – Generalize Designated Router to MANET Designated Routers (MDRs)
In an OSPF broadcast network, a single DR (red) is elected.
Each router becomes adjacent with the DR, forming a tree with n-1 edges.
In a multihop wireless network, the DR generalizes to multiple MDRs (red) which form a connected dominating set.
MDRs select themselves based on 2-hop neighbor information obtained from modified hello packets.
Adjacencies are formed between MDRs to form a connected backbone.
Each non-MDR becomes adjacent with an MDR neighbor called its Parent.

## Slide 6: Also Generalize Backup Designated Router for Biconnected Redundancy
In an OSPF broadcast network, a Backup DR (blue) is added for redundancy.
Each DR Other becomes adjacent with the DR and the Backup DR.
In a multihop wireless network, Backup MDRs (blue) are added to form a biconnected dominating set.
Backup MDRs perform backup flooding for improved robustness.
Optionally, additional adjacencies may be added to form a biconnected backbone, and each MDR Other may become adjacent with a second (Backup) MDR neighbor called its Backup Parent.

## Slide 7: Features of OSPF-MDR
MDRs and BMDRs are elected based on 2-hop neighbor information obtained from modified Hello packets.
If adjacency reduction is used (the default), adjacencies are formed between MDRs so as to form a connected backbone. An option (AdjConnectivity = 2) allows for additional adjacencies to be formed between MDRs/BMDRs to form a biconnected backbone.
Each non-MDR router becomes adjacent with an MDR called its Parent, and optionally (if AdjConnectivity = 2) becomes adjacent with another MDR or BMDR called its Backup Parent.
Each router advertises connections to its neighbor routers as point-to-point links in its router-LSA. Network-LSAs are not used.
In addition to full-topology LSAs, partial-topology LSAs may be used to reduce the size of router-LSAs. Such LSAs are formatted as standard LSAs, but advertise links to only a subset of neighbors.
Optionally, differential Hellos can be used, which reduce overhead by reporting only changes in neighbor states.

## Slide 8: Properties of OSPF-MDR in a Single-Hop Network
If adjacency reduction and full-topology LSAs are used, OSPF-MDR
running on a single-hop broadcast network has the following properties:
A single MDR is selected, which becomes adjacent with every other router (similar to OSPF).
If AdjConnectivity = 2 (biconnected), every non-MDR/BMDR router becomes adjacent with a BMDR in addition to the MDR (similar to OSPF).
Two BMDRs are selected. This occurs because the MDR selection algorithm ensures that the MDR/BMDR backbone is biconnected.
When all adjacencies are in Full state, the router-LSA for each router includes point-to-point (type 1) links to all bidirectional neighbors (in state 2-Way or greater).
Notes: Note that the first property on this slide is similar to both OSPF and draft-nsheth-ospf-hybrid-bcast-and-p2mp, but differs significantly from draft-retana-ospf-manet-single-hop, which results in a more random selection of adjacencies.

## Slide 9: Configuration in a Single-Hop Broadcast Network
When OSPF-MDR is used in a single-hop broadcast network, the following
parameter settings and options (defined in RFC 5614) should be used:
AdjConnectivity SHOULD be equal to 2 (biconnected), MAY be equal to 1 (uniconnected), and SHOULD NOT be equal to 0 (full topology).
An adjacency SHOULD be eliminated if neither the router nor the neighbor is an MDR or BMDR (see Section 7.3).
LSAFullness SHOULD be equal to 4 or 5 so that full-topology LSAs are originated. (The value 5 is a new option for single-hop networks.)
LSAFullness MAY be equal to 1 (min-cost LSAs) if full-topology LSAs are not required. This option reduces the number of advertised links while still providing shortest paths. (See Appendix C of RFC 5614.)

## Slide 10: Simplified Procedure for Selecting Neighbors to Advertise in LSAs
When using full LSAs, OSPF-MDR includes in its router-LSA point-to-point links for all fully adjacent neighbors, and all bidirectional neighbors that are routable.
A neighbor is routable if the SPT calculation has produced a route to the neighbor. (A flexible quality condition may also be required.)
In single-hop networks, the following alternative procedure may be used, which avoids having to update the set of routable neighbors:
  The MDR includes in its router-LSA a point-to-point (type 1) link for each fully adjacent neighbor. (Note that the MDR becomes adjacent with all of its neighbors.)
  Each non-MDR router includes in its router-LSA a point-to-point link for each fully adjacent neighbor, and, if the router is fully adjacent with the MDR, for each bidirectional neighbor j such that the MDR's router-LSA includes a link to j.

## Slide 11: Discussion of Alternative LSA Procedure
The new procedure implies that router i advertises a link to neighbor j only if router i is fully adjacent with the MDR, and the MDR is fully adjacent with router j.
Similarly, router j will advertise a link to router i only if it is fully adjacent with the MDR and the MDR is fully adjacent with router i.
Therefore, since the SPT calculation allows routers i and j to use each other as next hops only if they both advertise links to each other, the new procedure ensures that routers i and j are fully synchronized before they use each other as next hops.
The new procedure corresponds to LSAFullness = 5, and is interoperable with the other LSA options.
A similar (but not equivalent) procedure was proposed in draft-nsheth-ospf-hybrid-bcast-and-p2mp-01.
MDR
i
j

## Slide 12: Simplified MDR Selection Algorithm
The MDR selection algorithm of OSPF-MDR becomes much simpler in a single-hop network.
The resulting algorithm is similar to the DR election algorithm of OSPF, but not exactly the same.
  A single MDR is selected, but two BMDRs are selected so that the MDR/BMDR backbone is biconnected.
  As in an OSPF broadcast network, the number of resulting adjacencies is O(n).
In a single-hop network, the simplified algorithm described in the draft is equivalent to (and interoperable with) the full MDR selection algorithm.
Note: The DR election algorithm of OSPF can instead be used in single-hop networks if agreed by all routers. This would require a separate interface type for single-hop networks.

## Slide 13: Conclusions and Discussion
OSPF-MDR is an extension of OSPF that provides scalable routing in MANETs. In particular, it can be applied to single-hop broadcast networks in which different costs are assigned to different neighbors.
Recommended configuration settings are specified, and properties of OSPF-MDR are described when used in a single-hop network.
Two simplified procedures are specified when OSPF-MDR is used in a single-hop network. These procedures are optional, and are interoperable with unmodified OSPF-MDR.
If a network includes both (multihop) MANET interfaces and single-hop broadcast interfaces, then OSPF-MDR can be used for both interface types.
However, if the network includes only single-hop broadcast interfaces, a simpler solution is possible, e.g. draft-nsheth-ospf-hybrid-bcast-and-p2mp-01.
The partial-topology LSA option of OSPF-MDR may be useful in single-hop networks, to reduce LSA size and improve scalability.
Notes: The partial-topology LSA option of OSPF-MDR is called min-cost LSAs and is described in Appendix C of RFC 5614. Note that this makes sense for single-hop networks only if multiple interfaces are considered. Some simplification of this method may be possible for single-hop networks.