## Slide 1: OSPF Hybrid Broadcast and P2MP Interface Type
Nischal Sheth, Lili Wang, Jeffrey Zhang
Juniper Networks
81th IETF, Quebec City

## Slide 2: History
Initially presented in Beijing
Two polls on mailing list for WG adoption
  Have explicit support on the applicability and solution
  One objection in the first poll, citing MANET
    Resolved offline at 80th Prague meeting
      Problem and solution are independent of MANET
  No objection in the second poll

## Slide 3: Problem Context
True Broadcast Network
  Different metric for different neighbors
    But not MANET
Advertising per-nbr metrics
  But using broadcast network procedures for
    Neighbor maintenance
    DR/BDR based adjacency & flooding

## Slide 4: Plan
Waiting for WG blessing
Will plug one hole pointed out by Richard in the next revision
  Simple fix
MAY enhance on three aspects (which were already pointed out in 79th IETF)
  As part of WG effort

## Slide 5: Enhancements 1/3
Use Link Local Signaling to signal support
  this prevents adjacency with a non-supporting neighbor
    Otherwise traffic may not traverse certain pairs of routers
  Not a real/big problem if not done
    No persistent loop/blackhole

## Slide 6: Enhancements 2/3
Use LLS to signal information for neighbors to derive metric
  As another way to get per-nbr metric other than via:
    Static configuration
    Lower layer protocol, e.g. RFC 5578
  Example: routers connecting to a switch at 100M, 1G, 10G speeds
    All advertising their speed via LLS
    Router A (100M) derives metric 100 for all routers.
    All routers derive metric 100 for router A
    Router B (1G) derive 10 for router C/D (10G).
    Router C/D (10G) derives 10 for router B.
    Router C/D (10G) derives metric 1 for each other

## Slide 7: Enhancements 3/3
Advertising default metric, and additionally “odd” metrics that are different
  Vs. per-neighbor (reduce from O(N^2))
  Requires all routers to change SPF