## Slide 1: OSPF Traffic Engineering (TE) Express Path Updates draft-giacalone-ospf-te-express-path-01.txt
Spencer Giacalone, Alia Atlas, John Drake, Stefano Previdi, Dave Ward

## Slide 2: Overview
IETF 81
OSPF TE Express Path Automatically distributes network performance data
  Independent from measurement protocols and “applications”
Introduced at IETF 80
Updated to version 01 on May 30th 2011
<number>
Notes: <number>

## Slide 3: Efficiency Updates
Consolidated some sub-TLVs for efficiency
  No longer have nominal and anomalous sub-TLVs
  Steady and abnormal state data carried in two sub-TLVs (where we used to have four)
Anomalous (A) bit added to consolidated sub-TLVs
  Indicates whether the update pertains to normal or abnormal network performance state
  A bit is set when configured threshold(s) exceeded
  If A bit clear, sub-TLV represents steady state link performance
IETF 81
<number>
Notes: <number>

## Slide 4: Encoding Updates
Changed encodings of the variables in delay and jitter sub-TLVs from floating point to integer
  Allows reserved bit-space
  Provides space for A bit (when necessary)
  Permits common TLV structure across most sub-TLVs in the draft
Clarified how values are to be interpreted and added detail on units of measurement to address concerns about granularity and interoperability
IETF 81
<number>
Notes: <number>

## Slide 5: Structural Updates
Added sub-TLVs for Residual Bandwidth and Available Bandwidth
  Residual bandwidth is the Maximum Bandwidth [RFC3630] minus the bandwidth currently allocated to RSVP-TE LSPs
  Available bandwidth is the residual bandwidth (above) minus the measured bandwidth used for forwarding non-RSVP-TE LSP packets
IETF 81
<number>
Notes: <number>

## Slide 6: Other Updates
Made various clarifications across the draft
  Especially around thresholds and averaging
  Added a section on network stability
    Specified minimum inter-update timer
Agreed with CCAMP working group that OSPF encodings will remain in OSPF Express Path
Agreed to review CCAMP draft(s)
IETF 81
<number>
Notes: <number>

## Slide 7: Next Steps
IETF 81
<number>
Propose OSPF WG adoption
Revise draft
  Modifications based on feedback
Begin IS-IS TE Express Path draft
Begin application drafts (e.g. weighted ECMP)
Notes: <number>

## Slide 8
Questions
IETF 81
<number>