## Slide 1: Security Extension for OSPFv2 Using Manual Key Management
Manav Bhatia, Alcatel Lucent
Sam Hartman, Painless Security
Dacheng Zhang, Huawei Technologies
Acee Lindem, Ericsson
Notes: <number>

## Slide 2: Draft Overview
Defines new OSPFv2 AuthType for backward compatibility – Value of 3 suggested to IANA.
Extends OSPFv2 sequence number from 32 bits to 64 bits and partitions the sequence number space.
Defines keys selection rules with respect to draft-ietf-karp-crypto-key-table-00.txt.
Protects IP source address with cryptographic hash.
Notes: <number>

## Slide 3: Sequence Number Extension (1/3)
Current sequence number weaknesses
  Monotonically increasing
  Only 32 bits – no provision for router restart
New AuthType Sequence Number
  Strictly increasing
  64 bits – 32 bits of boot count and 32 bits of sequence number
  Moved out of OSPFv2 header auth data
Notes: <number>

## Slide 4: Sequence Number Extension (2/3)
Boot Count
  Maintained in non-volatile storage for the life of the deployed router.
  Incremented each time OSPF router loses its state.
  Can also be incremented if low order sequence number wraps
Sequence Number is incremented for every OSPFv2 packet sent
Notes: <number>

## Slide 5: Sequence Number Extension (3/3)
Receiver drops packet if received packet’s sequence number is not greater than previously received OSPF packet of same type – handles prioritization of hellos and acks.
64 bit sequence number follows OSPF packet but before authentication data
  Doesn’t fit in OSPFv2 header
  Not in OSPFv2 length
  Included in IP packet length
Notes: <number>

## Slide 6: Key Selection Rules Mapping Key Database
Mapping to Database of Long-Lived Symmetric Cryptographic Keys <draft-ietf-karp-crypto-key-table-01.txt>
Key Mapping for Unicast transmission
  Currently problem with virtual links
Key Mapping for Multicast transmission
Key Mapping for Reception
Discussion on usefulness of this section or normative reference to key database draft.
Notes: <number>

## Slide 7: IP Source Address Protection
Currently unprotected – Source IP address used by OSPFv2 for OSPF router identification on broadcast and NBMA networks
IP Source Address replaces Apad in cryptographic authentication as described in RFC 5709, section 3.3.
Apad is a hexadecimal constant value 0x878FE1F3 repeated (L/4) times, where L is the length of the hash in bytes.
Notes: <number>

## Slide 8: Next Steps
Revision Forthcoming
Determine if Key Selection useful in the context of this draft
Review and discussion on the OSPF list
Notes: <number>

## Slide 9: Review of Proposed Changes
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Version # | Type | Packet length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Router ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Area ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Checksum | AuType (3) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 0 | Auth Data Len |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Key ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
| OSPF Protocol Packet |
~ ~
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number (Boot Count) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number (Strictly Increasing Packet Counter) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
~ Authentication Data ~
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Notes: <number>