## Slide 1
Dean Cheng (dean.cheng@huawei.com)
Mohamed Boucadair (mohamed.boucadair@orange-ftgroup.com)
811st IETF Quebec City
Routing IPv4-Embedded IPv6 Packets
draft-ietf-ospf-ipv4-embedded-ipv6-routing-00
1

## Slide 2: Status Update
draft-cheng-ospf-ipv4-embedded-ipv6-routing-01 was presented in Beijing meeting
  Proposed as an informational RFC
  One suggestion from Acee was incorporated into 02 text afterwards
Comments were solicited from BEHAVE/SOFTWIRE WG chairs and Joel Halpern with some discussions
  There were no opposition to the draft
  Some clarifications were made during discussions
  03 text was published afterwards
Adopted as OSPF WG document shortly after Prague meeting
  There were some support on the mailing list during the WG poll
  draft-ietf-ospf-ipv4-embedded-ipv6-routing-00
  One e-mail exchange (Nagendra Kumar) on the mailing list recently
2

## Slide 3: Some Terminologies
IPv4-embedded IPv6 address
  Denotes an IPv6 address which contains an embedded 32-bit IPv4 address constructed according to the rules defined in:
  RFC6052 (IPv6 Addressing of IPv4/IPv6 Translators )
IPv4-embedded IPv6 packets
  IPv6 packets with destination addresses as IPv4-embedded IPv6 addresses
AFXLBR
  Address Family Translation Border Router
  Refers to a border router which is located at the boundary of an IPv6-only network and an IPv4-only network, supports both IPv4 and IPv6 address family, and performs IPv4-IPv6 header translation per RFC6145 (IP/ICMP Translation Algorithm)
3

## Slide 4: The Problem
ASBR
IPv6
IPv6
IPv6 backbone
IPv4
IPv6
IPv4
IPv4
ASBR
AFBR
AFBR
AFBR
?
?
?
4
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5: Softwire Mesh (RFC5565) Approach
ASBR
IPv6
IPv6
IPv6 backbone
IPv4
IPv6
IPv4
IPv4
ASBR
AFBR
AFBR
AFBR
AFBRs exchange IPv4 reachability using BGP-MP
Tunnels established between AFBRs full-mesh
IPv4 packets transported in tunnels
5
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: OSPFv3 MT/MI Approach
ASBR
IPv6
IPv6
IPv6 backbone
IPv4
IPv6
IPv4
IPv4
ASBR
AFXLBR
AFXLBR
AFXLBR
AFXLBRs advertise IPv4-embedded IPv6 addresses into the partial IPv6 backbone
A separate routing table for routing IPv4-embedded IPv6 packets.
6
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: Scenarios where OSPFv3 approach useful
Running BGP not feasible sometimes
Tunnel based forwarding not feasible
IPv4
IPv4
CPE
IPv6 Network
IPv4
CPE
CPE
CPE
CPE
CPE
CPE
ICXF
ICXF
AFTR
AFTR
AFTR
ICXF
IPv6
IPv6
Dual-Stack
DS-Lite
One use case: draft-boucadair-softwire-dslite-v6only-01
7

## Slide 8: Mechanisms for separate routing table
Use OSPFv3 multi-instance mechanism
  Reference: RFC5838
  Instantiate a separate instance for IPv4-embedded unicast IPv6 routing
Use OSPFv3 multi-topology mechanism
  Reference: http://tools.ietf.org/html/draft-ietf-ospf-mt-ospfv3-03.txt
  Configure interfaces for IPv4-embedded unicast IPv6 routing
8

## Slide 9: Advertising IPv4-Embedded IPv6 Routes
IPv4-embedded IPv6 addresses would be advertised by AFXLBR into IPv6 network as AS External LSA per OSPFv3(RFC5340)
  A single OSPFv3 AS External LSA carries one IPv4-embedded IPv6 address or prefix
  The metric
    By default, it is type-1 metric
    May also be set to type-2 metric (by provisioning at AFXLBR)
  No forwarding address
    Let AFXLBR performs IPv4 routes look-up
9

## Slide 10: Forwarding IPv4-Embedded IPv6 Packets
At AFXLBR
  Packet header translation
    According to RFC 6145 (IP/ICMP Translation Algorithm)
  Address translation
    According to RFC6052 (IPv6 Addressing of IPv4/IPv6 Translators )
  IPv6 prefix
    Well known IPv6 prefix 64::FF9B::/96, or
    ISP-specific IPv6 prefix
At other IPv6 routers
  Arriving packets with IPv4-embedded IPv6 addresses are forwarded along on IPv4-embedded IPv6 topology.
MTU handling
  Recommendation – AFXLTR to run PMTU (RFC1981)
10

## Slide 11: Next Step …
Authors would like to solicit comments with discussion on mailing list at this time
Will update the draft accordingly later
11