## Slide 1: Mobile Multicast Sources Support in PIMIPv6 Domains
Presenter: Shuai Gao
2011.11.15
draft-schmidt-multimob-pmipv6-base-source-01
draft-zhang-multimob-msm-03

## Slide 2: Objective of the Drafts
Describes the support of mobile multicast sources at basic deployment of multicast support in PMIPv6 domains.
Discusses some open issues, including PIM neighbors, route optimizations, LMA suppressions.

## Slide 3: Multicast Base Deployment with Mobile Source
+-------------+
| Multicast |
| Receivers |
+-------------+
/ \
+----+ +----+
|LMA1| |LMA2| Multicast Anchor
+----+ +----+
LMAA1 | | LMAA2
| |
\\ //\\
\\ // \\
\\ // \\ Unicast Tunnel
\\ // \\
\\ // \\
\\ // \\
Proxy-CoA1 || || Proxy-CoA2
+----+ +----+
|MAG1| |MAG2| MLD Proxy
+----+ +----+
| | |
MN-HNP1 | | MN-HNP2 | MN-HNP3
MN1 MN2 MN3
Multicast Senders & Receivers
DR or MLD Proxy
MLD Proxy forwards locally and per Uplink

## Slide 4: Open Issues 1
PIM DR direct connection check problem at the LMA
  LMAs acting as DR in PIM [RFC4601] will require sources to be directly connected for sending PIM registers to the RP. This does not hold in a PMIPv6 domain, as MAGs are routers intermediate to MN and the LMA.
  Solutions: LMA should act as a PIM Border Router (PMBR).
    the DirectlyConnected(S) is treated as being TRUE for mobile sources.
    Working at the incoming tunnel interface. Don’t interfere normal multicast functions at other physical interfaces.
    Some indication mechanism to switch on or off the PMBR function with the movement or access change of multicast sources?

## Slide 5: Open Issues 2
Routing is optimal for receivers at the sender’s MAG that belong to the same LMA, and for the fixed Internet
Routing detours via LMAs, whenever
  Mobile listener is attached to another MAG
  Mobile listener is associated with a different LMA
Possible solutions
  Direct Routing:
    Up-link of MLD-proxy at the MAG into multicast cloud. PIM neighbor problem for the multicast sources?
    MAG acts as DR?
    Delay and handover cost during the movement of sources
  Multi-Upstream Interfaces MLD Proxy

## Slide 6: Open Issues 3
The LMA will receive all multicast traffic originating from its associated MNs regardless whether there are receivers or not.
Solutions
  Admission control mechanisms like source-stop scheme between LMAs and MAGs may be added to suppress multicast flooding to LMAs, if there’s no corresponding receivers
  set a timer for resending data from MAGs if needed.

## Slide 7: Status of the draft & Next Step
A merged version of the proposed two drafts.
The new draft will explain source mobility in the base scenario.
The new draft will explore the direct routing option for sources.
Optimization approaches will be included.

## Slide 8
Questions
Thank You!