## Slide 1: Rapid acquisition of the MN multicast subscription after handover <draft-contreras-multimob-rams-03.txt>
Luis M. Contreras
Telefónica I+D
Carlos J. Bernardos
Universidad Carlos III de Madrid (UC3M)
Ignacio Soto
Universidad Politécnica de Madrid (UPM)
Taipei, MULTIMOB WG, November 2011
1

## Slide 2: Proposal Status
82nd IETF, Taipei
Initial draft version submitted for 78th IETF meeting in Maastricht
Proposal included in re-chartering discussion during 78th IETF
Draft presented in Beijing (79th) and Quebec (81st) IETF meetings
Updated version submitted for 82nd IETF:
draft-contreras-multimob-rams-03.txt
  New text addresses the potential benefits of the co-existence of layer-2 triggers for fast handover able to forward traffic to the new MNs point of attachment
2

## Slide 3: Draft motivation and advantages
82nd IETF, Taipei
The draft covers the MULTIMOB charter goal of optimizing multicast traffic during a handover
It is a generic process, nor dependent on layer-2 trigger capacities of the radio technology in use
  Despite it could be beneficial if traffic forwarding is implemented
It keeps simple the management, control and data plane functions at the MAG
  Traffic forwarding through layer-2 triggers can be handle as optinial, while tha goal of optimizing the handover is kept
It is based on the transfer of information through homogeneus high-bandwidth links among carrier-class devices
It is based on the information provided by the pMAG which definitely ensures the correctness about the subscription information
  When using fast HO for PMIPv6 (RFC5949) the UL path is moved to the new access network after DL does. In this condition, an MLD Report from MN sent in the meantime will be attended by pMAG, while the nMAG will ignore it, causing service disruption
3