## Slide 1: Multicast Fast Handover: Context Transfer for Mobility Protocol Standards draft-schmidt-multimob-fmipv6-pfmipv6-multicast-05
Thomas C. Schmidt, Matthias Wählisch, Rajeev Koodli, Gorry Fairhurst

## Slide 2: PFMIPv6 Predictive Handover
PMAG NMAG
MN P-AN N-AN (PAR) (NAR)
| | | | |
| Report | | | |
|---(MN ID,-->| | | |
| New AP ID) | | | |
| | HO Indication | |
| |--(MN ID, New AP ID)-->| |
| | | | |
| | | Optional: |
| | | MLD Query |
| | | | |
| | | |------HI---->|
| | | |(Multicast MobOpt)
| | | | |
| | | |<---HAck-----|
| | | |(Multicast AckOpt)
| | | | |
| | | | Join to
| | | | Multicast
| | | | Groups
| | | | |
| | | |HI/HAck(optional)
| | | |<- - - - - ->|
| | | | |
| | | optional: forward |
| | | packets =======>|
disconnect | | | |
| | | | |
connect | | | |
| MN-AN connection | AN-MAG connection |
|<----establishment----->|<----establishment------->|
| | | (substitute for UNA) |
| | | | |
|<========================================== deliver packets
| | | | |
2

## Slide 3: Design Objectives
Optimize for seamless handover
  Synchronize multicast with fastest unicast operations
Generic approach: works for PMIP + MIP
  Generic messaging: Mobility options + MLD
Align with mobility protocols
  Transparently plug in multicast of all flavors
Abstract from multicast routing
  Remain independent of routing solution
Simplify protocol extensions
  Use existing message structures
3

## Slide 4: Why Context Transfer Between ARs / MAGs?
Because this is the fastest possible approach:
does not work well with direct routing and puts additional burden to LMA
LMA
MAG
MAG
≤
4

## Slide 5: Why Use Unicast Protocol(s) (P)FMIP?
Seamless multicast handover requires synchronization with Unicast
  No service without unicast connectivity
  Misalignment may lead traffic into the wild
  Different issue: vertical mcast access
(P)FMIP are the unicast protocols for inter-AR signaling
  We are not chartered to invent new unicast handover management
5

## Slide 6: Isn‘t (P)FMIP too Heavy-Weight?
(P)FMIP provides two functions:
Context transfer between ARs (minimal operation of control plane)
Fast forwarding / buffering at the data plane (now optional for multicast)
6

## Slide 7: What is worse: Packet re-ordering or loss?
Fast handover introduces re-routing / fast forwarding and thus may re-order packets
  In the presence of buffering at ARs/MAGs, packet loss is prevented
Base Solution and LMA-based redirection cause packet loss
  Packets arriving too late at pAR/pMAG go bust
  Buffering at LMA is a severe scaling issue
7

## Slide 8
Questions/Comments?
8