## Slide 1: PMIPv6 Extension for Multicast draft-asaeda-multimob-pmip6-extension-07
Hitoshi Asaeda
Pierrick Seite
Jinwei Xia
82nd IETF, November 2011, Taipei, Taiwan

## Slide 2: Background
Address tunnel convergence problem
  Both LMA and MAG act as PIM-SM routers
    Support both ASM and SSM
  Incoming IF on LMA/MAG is selected by an RPF lookup algorithm given by PIM
Support local/direct routing
Source mobility friendly
  But out of scope of this document
Mobility support (i.e. seamless handover)
  Scenario 1: With Policy Profile
    When MN’s subscribing channel list is always maintained
  Scenario 2: With multicast extended PBU/PBA
    Use DeReg PBU and PBA having multicast channel information (PBU-M/PBA-M)

## Slide 3: Changes from -06
Simplify the scenario
  Remove M-Tunnel
    Usually use bi-directional tunnel
  Assume to copy unicast routing table (e.g. RIB) to MRIB
Editorial changes

## Slide 4: Basic Data Flow – Example
MAG and LMA act as PIM-SM routers
  Upstream IF for (S1,G1) is LMA-MAG Bidirectional Tunnel IF
  Upstream IF for (S2,G2) is MAG’s physical IF (e.g. direct routing)
MN1
MN2
MAG
LMA
MLD Report
(S2,G2)
PIM join
Bidir Tunnel
MLD Report
(S1,G1)
(S1,G1)
PIM join
PIM join
(S1,G1)
(S2,G2)

## Slide 5: Handover Example 1
Fixed Internet
LMA1
nMAG
Src
MN
MN
MN
Bidir Tunnel
PIM-SM
enable
router
PIM Join
Src
LMA2
pMAG
PMIPv6-Domain
MN
PBU/PBA
PBU-M
(DeReg)
/PBA-M
Src
MR

## Slide 6: Handover Example 2
Fixed Internet
LMA1
nMAG
Src
MN
MN
MN
Bidir Tunnel
PIM-SM
enable
router
Src
LMA2
pMAG
PMIPv6-Domain
MN
PBU/PBA
PBU-M
(DeReg)
/PBA-M
Src
MR
PIM Join

## Slide 7: Handover Scenario – Home Subscription
MN p-MAG LMA n-MAG
| | | |
|----- MLD Report ---->| | |
| |==Bidir Tunnel(PIM join)==>| |
| | |---> PIM join |
|<---------------------|<=Bidir Tunnel(Multi.data)=| |
| | | |
Detach | | |
| MN detachment event | |
| |------- DeReg PBU-M ------>| |
| | (Acquire multicast channel |
| | information for MN-ID) |
| | Accept PBU |
| |<---------- PBA -----------| |
Attach | | |
| | | MN attachment event (Acquire MN-ID)
|------------------------------------ RS ------------------------------------->|
| | |--------- PBU -----------|
| | |---------- PBA-M --------->|
| | | (Acquire multicast channel
| | | information for MN-ID)
| | |<==Bidir Tunnel(PIM join)==|
|<----------------------------------- RA --------------------------------------|
| | |=Bidir Tunnel(Multi.data)=>|
|<--------------------------------- Multicast data ----------------------------|
| | | |

## Slide 8: Handover Scenario – Remote Subscription (or Direct Routing)
MN p-MAG LMA n-MAG
| | | |
|----- MLD Report ---->| | |
| |---> PIM join | |
|<-- Multicast data ---| | |
| | | |
Detach | | |
| MN detachment event | |
| |------- DeReg PBU-M ------>| |
| | (Acquire multicast channel |
| | information for MN-ID) |
| | Accept PBU |
| |<---------- PBA -----------| |
Attach | | |
| | | MN attachment event (Acquire MN-ID)
|------------------------------------ RS ------------------------------------->|
| | |--------- PBU -----------|
| | |---------- PBA-M --------->|
| | | (Acquire multicast channel
| | | information for MN-ID) |
| | | |---> PIM join
|<----------------------------------- RA --------------------------------------|
|<----------------------------------- Multicast data --------------------------|
| | | |

## Slide 9: Proxy Binding Update with Multicast Channel Information (PBU-M)
Extension for PMIPv6 [RFC5213]
New “multicast subscription flag (C)”
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence # |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|A|H|L|K|M|R|P|C| Reserved | Lifetime |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
. .
. Mobility options .
. .
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 10: Proxy Binding Acknowledgement with Multicast Channel Information (PBA-M)
Extension for PMIPv6 [RFC5213]
New “multicast subscription flag (C)”
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Status |K|R|P|C|Reserve|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence # | Lifetime |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
. .
. Mobility options .
. .
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 11: Mobility Options in PBU-M/PBA-M
The format of the Mobility options field uses the TLV format defined in [RFC3775] where the field contains Multicast Address Record with the same definitions in [RFC3810].
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type = TBD | Length |Nr of Mcast Address Records (M)|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
. .
. Multicast Address Record [1] .
. .
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
. .

## Slide 12: Conclusion
This draft describes PMIPv6 with PIM-SM
  Address tunnel convergence problem
  Support mobility
WG item?