## Slide 1: Tuning the Behavior of IGMP and MLD for Routers in Mobile and Wireless Networks
draft‐ietf‐multimob‐igmp‐mld‐tuning-02
Hitoshi Asaeda
Hui Liu
Qin Wu
82nd IETF, November 2011, Taipei, Taiwan

## Slide 2: Summary
This document describes the ways of IGMPv3 and MLDv2 protocol optimization for mobility, and aims to become a guideline for query and other timers and values tuning.
Potential tuning values are clarified
  Query Interval
  Query Response Interval
  Last Member Query Timer (LMQT) / Last Listener Query Timer (LLQT)
  Startup Query Interval
  Robustness Variable

## Slide 3: Changes
Explicit tracking function
  Normative reference -> Informative reference
  SHOULD -> recommend
Editorial changes

## Slide 4: Query Interval (125 sec.)
150 sec.
  For a wireless link having a number of nodes (e.g.,200 nodes)
  Pro.
    Minimizing traffic of Report messages and battery power consumption for mobile hosts
60 to 90 sec.
  For a wireless link having a higher capacity of the resource
  Pro.
    Quick synchronization of the membership information tracked by the router

## Slide 5: Query Response Interval (10 sec.)
10 to 20 sec.
  For a wireless link having a lower capacity of network resource (e.g., a bursty IEEE 802.11b link) or for a lossy link
  Pro.
    Reduce congestion of the Current-State Report messages on a link
  Con.
    Increase join latency and leave latency when the unsolicited messages (State-Change Record) are lost on the router
5 to 10 sec.
  For a wireless link having enough capacity (e.g., an IEEE 802.16e link) or reliable condition for IGMP/MLD message transmission
  Pro.
    Quick discover of non-tracked member hosts and synchronization the membership information

## Slide 6: LMQT and LLQT (2 sec.)
LMQT (=LMQC (Rob. Var.) * LMQI (1))
1 sec.
  LMQC=1, LMQI=1
    For a reliable link, LMQI can be smaller, e.g. 0.5, then LMQT=0.5 sec.
  Pro.
    Shortening leave latency
  Con.
    There is a risk that a router misses Report messages from remaining members if the router adopts small LMQC/LLQC
    However the wrong expectation would be lower happened for the router enabling the explicit tracking function.
2 sec.
  LMQC=2, LMQI=1
  For a wireless link being lossy (e.g., due to a large number of attached hosts or limited resources)

## Slide 7: Startup Query Interval (1/4 of [Query Interval] (e.g. 25 sec.))
1 sec. (or shorter than 1 sec.)
  Time to discover members when link is up
  Shortening handover latency

## Slide 8: Robustness Variable (2)
2
  In the regular case
1
  For a wireless link having higher capacity of the resource or reliable condition
Note
  SHOULD NOT be bigger than 2 in a wireless env.

## Slide 9: Tuning Scenarios for Various Mobile IP Networks
Three deployment scenarios
  IGMP/MLD running directly between host and access router on a wireless network
    Base condition
  IGMP/MLD running between host and home router through a tunnel link
    Shorter [Query Interval] and [Query Response Interval], and two or more [Robustness Variable] value
      Because message transmission depends on the condition of the tunnel link
  IGMP/MLD running between home router and foreign router through a tunnel link (e.g. RFC6224)
    [Query Response Interval] on the home router or local mobility anchor could be set to the smaller value
      Because the number of foreign router is much smaller than usual

## Slide 10: Next Step
WGLC?
  Intended status: Informational?