## Slide 1: Multicast handover discussion
Marco Liebsch
IETF82, Taipei
Multimob WG
15th November 2011

## Slide 2
…meant as input to the discussion towards finding a good choice for a protocol base

## Slide 3: Techniques on the table
Early and/or fast join of the new MAG to the MC group to receive relevant content
  Proactive transfer of group and source context from pMAG to nMAG
  2 approaches: inter-MAG CTX transfer or CTX transfer via LMA
Immediate delivery of MC packets from new MAG to MN after handover
  Proactive transfer of MN information may not help
  MC router must wait until signal from MN received
  Attach can trigger a Query from nMAG
Forwarding of MC data from pMAG to nMAG
  Avoid missing MC packets

## Slide 4: Forwarding of MC data from pMAG
Can help to avoid missing MC packets in case..
  nMAG has not joined the MC group before
  high latency in nMAG joining the MC group
  nMAG buffers forwarded MC packets
  client can buffer all packets after delivery when attached to nMAG
  client plays buffered packets without dropping them
    Real time data?

## Slide 5: Forwarding of MC data from pMAG
For further consideration..
  How to treat duplicated packets on the nMAG?
    Forwarded and received on MC channel
    Which ones to forward?
  Default client may use only small buffer
  Default client may drop delayed packets
    If not, it continues playing them with permanent delay
  Reordering
    Solve it on Client or on nMAG?
    Don’t address it?
  If forwarding is optional, who decides using it?
    Dynamic protocol component?
    Static setting by means of Administration / Operator?

## Slide 6: nMAG joining the MC group
Alignment of Unicast and Multicast handover has been mentioned as requirement
However, most important seems a common handover target (nMAG)
Beside that, Unicast and Multicast states..
  can be established at different timing
    State about MC group to join can be established on nMAG before unicast state (most time critical)
  can be established using different protocols
CTX approach may depend on available security associations
  Inter-MAG vs. transfer via LMA… both have pros and cons

## Slide 7: Impact on MC Router operation
nMAG joins MC group and sources based on CTX transfer mechanisms
nMAG may send MC Query to MN immediately after attach
How much is the impact on standard MC Router operations?