## Slide 1: Mobile Multicast Sender Support in PMIPv6 Domains draft-ietf-multimob-pmipv6-source-01
Thomas C. Schmidt
t.schmidt@ieee.org
HAW Hamburg

## Slide 2: Objective of the Draft
Define Multicast Source Mobility for PMIP
Three Basic Multicast Scenarios:
Base-line approach compliant to RFC 6224:
  Simple, directly reflects PMIP routing
Direct Multicast Distribution
  Based on Proxies, PIM-S(S)M or BIDIR PIM
Optimized Source Mobility
  Extended Proxies for traffic optimization

## Slide 3: Document History
Initial version draft-ietf-multimob-pmipv6-source-00
  Presented in Paris
Current version draft-ietf-multimob-pmipv6-source-01
  Direct routing with PIM-SM and PIM-SSM has been added.
  PMIP synchronization with PIM added for improved handover.
  Direct routing with BIDIR-PIM has been added.
  MLD Proxy extensions requirements added.
  Peering of MLD Proxies added.
  First sketch of multiple upstream proxy added.

## Slide 4: 1. Base Solution
Deployment as of RFC 6224
  MLD Proxy at MAG (one instance per LMA-uplink)
  Multicast router (or another proxy) a LMA
Direct forwarding at MAG to LMA upstream and directly attached downstreams
  Compliant to PMIP routing rules
Transparent to ASM and SSM
Performance:
  Good for truly remote & directly attached listeners
  Poor for MNs associated to different LMA

## Slide 5: 2. Direct Multicast Routing

## Slide 6: 2.1 Single Proxy at MAG
MLD Proxy uplinks to ‘multicast cloud’
  Single instance uplinked (tunneled) to multicast domain
  Approach compliant to MTMA-scheme
Some specifics for multicast routing in the ‘cloud’
  PIM-SM: source not directly connected
  PIM-SSM: source-specific routes need reconstruction on handover, which may delay service

## Slide 7: 2.2 PIM-SM at the MAGs
Problem: Use meaningful MRIB independent of PMIP unicast
  Keep access network flat to avoid tardy re-routing
Consider the three phases of PIM-SM
  Phase 1: Source register (tunneling)
    Fairly fast & simple, complies to source mobility
  Phase 2: Source-specific RP tree
    Routes via RP + LMAs, fallback to phase 1 on HO
  Phase 3: Source-specific shortest path tree
    Routes via LMAs, fallback to phase 1 on HO
Handover optimization:
  Synchronize multicast state maintenance with unicast handover

## Slide 8: 2.3 BIDIR-PIM at the MAGs
Requires meaningful MRIB independent of PMIP unicast
  In contrast to PIM-SM, only routes to static entities required
BIDIR-PIM is agnostic to source mobility
  Mobile source transmits data towards the RPA
  On handover: Can resume transmission immediately after unicast reconfigurations
BIDIR-PIM can be considered the protocol of choice for direct routing in a PMIP domain

## Slide 9: 3. Optimized Source Mobility
Scenario: Proxies at MAGs
Objective: Optimize traffic exchange from a local MAG - including policy implementations
Requirements:
  Unique coverage of receivers
  Prevention of Routing Loops
Multiple upstream proxy for sources (MUIMP)
  Traffic forwarded to multiple LMAs
Proxy Peering Interface (PPI)
  Horizontal traffic exchange between proxy instances

## Slide 10: 3.1 Multiple Upstream Proxy
Unambiguously guide traffic to upstream interfaces
Sketch:
  Apply filters at interfaces (*,G), (S,*)
Details: Work in progress

## Slide 11: 3.2 Proxy Peering
Defines new interface type: Peering
  Established between any two proxy instances for shortcutting traffic
  Silent virtual link in regular proxy operations
Proxy will filter for local sources at peering link  avoid routing loops
  Regular downstream will not traverse peering link
  Local source traffic will be forwarded on MLD-report
Proxy listener will avoid duplicate traffic
  ASM: Prefer peering link, filter regular upstream
  SSM: Apply source filters according to preference

## Slide 12
Questions?