## Slide 1: Network Overlay Dataplane Requirements
Draft-nb-nvo3-dataplane-requirements-01

## Slide 2: Authors
Nabil Bitar
Marc Lasserre
Florin Balus
Thomas Morin

## Slide 3: Purpose of the draft
Dataplane requirements for Data Center Network Virtualization over L3 tunnels:
  VAP Identification
  L2 & L3 VNI types
  NVO3 header and tunnel processing
  VN context identification
    Explicit unique id (e.g. VNID) or locally significant identifier
  Optional QoS/Cos marking
  NVE tunnelling functions
    IP encaps (MUST) & MPLS encaps (MAY)
    LAG & ECMP support
    DiffServ & ECN marking
  BUM handling
  External connectivity via GW
  Path optimality
  Path MTU handling

## Slide 4: VNI Types
L2 VNI
  Emulated Ethernet multipoint service
  MAC address learning via
    Dataplane learning
    Control/Management plane MAC address population
L3 VNI
  Virtualized IP routing & forwarding

## Slide 5: Changes in -01
Addressed comments made on the list and privately
  Updated VN context identification (VNID or local reference ID)
  Optional multicast support
  Optional integrated bridging & routing support
  Clarification of DP learning applicability vs CP/Management based provisioning

## Slide 6: Next Steps
Make entropy requirement more generic
  E.g. “the encapsulation MUST result in sufficient entropy to exercise all paths through several LAG/ECMP hops”