## Slide 1: draft-ashwood-nvo3-operational-requirement-00.txt July 2012
Peter Ashwood-Smith - peter.ashwoodsmith@huawei.com Ali Sajassi - sajassi@cisco.com

## Slide 2: Two approaches
We can go bottom up, i.e. add requirements as we go.
  Pro: Light weight, Con: less complete.
We can go top down, i.e. take existing requirements and cut down.
  Con: Heavier weight, Pro: more complete.

## Slide 3: We chose to go top down
There is a wealth/dearth of OAM work already done so we went looking for existing requirements (I’m lazy).
Within the IETF we used RFC 6136 as a base .. which in turn builds on OSI OAM.
“Layer 2 Virtual Private Network (L2VPN) Operations Administration, and Maintenance (OAM) Requirements and Framework. March 2011 A. Sajassi and D. Mohan.”
Yes this is overkill and needs pruning but feel that’s a group exercise.

## Slide 4: Stealing RFC 6136 requirements and re-homing for NVO3 with little pruning yet yields ...
R1) NVO3 OAM MUST allow an NV Edge device to discover other NV Edge devices that share the same VNI within a given NVO3 domain.
R2) NVO3 OAM MUST allow proactive connectivity monitoring between two NV Edge devices that support the same VNIs within a given NVO3 domain.
R3) NVO3 OAM MUST allow monitoring/tracing of all possible paths between NV Edge devices such that equal cost paths that traverse LAG and/or ECMP may be differentiated.

## Slide 5: Cont’d ..
R4) NVO3 OAM MUST allow connectivity fault verification between two NV Edge devices that support the same VNI within a given NVO3 domain.
R5) NVO3 OAM MUST allow connectivity fault localization between two NV Edge devices that support the same instance within a given NVO3 domain.
R6) NVO3 OAM MUST support fault notification to be triggered as a result of the IP underlay network faults. This fault notification SHOULD be used for the suppression of redundant service-level alarms.

## Slide 6: Cont’d ..
R7) NVO3 OAM MUST support measurement of per VNI frame/packet loss between two NV Edge devices that support the same VNI within a given NVO3 domain.
R8) NVO3 OAM MUST support measurement of per VNI two-way frame/packet delay between two NV edge devices that support the same VNI within a given NVO3 domain.
R9) NVO3 OAM SHOULD support measurement of per VNI one-way frame/packet delay between two NV Edge devices that support the same VNI within a given NVO3 domain.

## Slide 7: Cont’d ..
R10) NVO3 OAM MUST support measurement of per VNI frame/packet delay variation between two NV Edge devices that support the same VNI within a given NVO3 domain.
R11) NVO3 OAM frames MUST be forwarded along the same path (i.e., links (including LAG members) and nodes) as the NVO3 data frames.
R12) NVO3 OAM frames MUST provide a mechanisms to exercise/trace all data paths that result due to ECMP/LAG hops.

## Slide 8: Cont’d ..
R13) NVO3 OAM MUST be scalable such that an NV edge device can support proactive OAM for each VNI that is supported by the device. (Note - Likely very hard to achieve with hash based ECMP/LAG).
R14) NVO3 OAM MUST be extensible such that new functionality and information elements related to this functionality can be introduced in the future.
R15) NVO3 OAM MUST be defined such that devices not supporting the OAM are able to forward the OAM frames in a similar fashion as the regular NVO3 data frames/packets.

## Slide 9: Cont’d ..
R16) NVO3 OAM frames MUST be prevented from leaking outside their NVO3 domain.
R17) NVO3 OAM frames from outside an NVO3 domain MUST be prevented from entering the NVO3 domain when such OAM frames belong to the same level or to a lower-level OAM. (Trivially met because hierarchical domains are independent technologies)
R18) NVO3 OAM frames from outside an NVO3 domain MUST be transported transparently inside the NVO3 domain when such OAM frames belong to a higher-level NVO3 domain. (Trivially met because hierarchical domains are independent technologies).

## Slide 10: Cont’d ..
R19) NVO3 OAM MAY allow adaptation/inter-working with its IP underlay OAM functions. For example, this would be useful to allow fault notifications from the IP layer to be sent to the NVO3 layer and likewise exposure of LAG / ECMP will require such non-independence.
R20) NVO3 OAM MUST be independent of the application technologies and specific application OAM capabilities.

## Slide 11: Next Steps
Add/Remove requirements.
Track removed requirements and reason to avoid future debates.
Needs email debate.