## Slide 1: FMC BoF IETF 85 Requirements in Fixed Mobile Convergence draft-schott-fmc-requirements-04
Roland Schott

## Slide 2: Motivation for Us #1
From the service provider perspective Fixed Mobile Interworking it is the ability to deliver any service with any device at any time and anywhere.
Converged Business Models
Converged Services
Converged Network & Infrastructure
Converged User Management &
Terminals
2012/11/6
2
FMC BoF IETF 85 Atlanta

## Slide 3: Motivation for Us #2
Fixed Mobile Interworking in context of Multi Access Connectivity to IP networks and services.:
Ubiquitous consumption of data and efficient resource usage call for integrated access to fixed and mobile networks
Most smartphones today allow for multiple options to access the network e.g. via WiFi and cellular technology
Seamless service provisioning via Fixed Mobile Interworking/Integrated infrastructure demands for bunch of new features supporting highly heterogeneous access technologies on potentially different administrative domains with different AAA entities, mobility anchors (such as)
  Proper access technology selection
  UE identity handling (user mobility)
  Subscriber/Group identity handling (service mobility)
  UE mobility across domains
  Link quality information for service adaptation and connectivity policy
  …
2012/11/6
3
FMC BoF IETF 85 Atlanta

## Slide 4: Why Standardization is needed?
Current Status of ID Handling:
Subscriber/Group Identity handling (service mobility) & device handling:
  Multi-SIM
  Access Identification in fixed networks for plug & play by using specific ID format
  …
Characteristic
  focusing on specific problems & networks, not FMC
  proprietary
Goal for a standardized subscriber/group ID:
  to achieve network synergies & seamless services
  low cost
  independent of access
  secure
  useful for various use cases
2012/11/6
4
FMC BoF IETF 85 Atlanta

## Slide 5: Network Architecture Evolution
Control protocols and functional modules to support operator and user chosen policies within network and terminal nodes:
2012/11/6
5
FMC BoF IETF 85 Atlanta
IP Network
IP Network
Operator IP Network
UE
3G/4G BS
Internet
Operator IP Network
PCRF
mAAA
BPCF
fAAA
Real time
streaming
Delay tolerant
Service platform
UE
UE
WiFi AP
RG
H(e)NB
RG
AAA Authentication Authorization Accounting
AP Access Point
BS Base Station
BPCF Broadband Policy Control Function
fAAA AAA in fixed network
H(e)NB Home (evolved) NodeB
mAAA AAA in mobile network
PCRF Policy Charging Rule Function
RG Residential Gateway
UE User Equipment
Heterogeneous Access

## Slide 6: Requirement #1: Group Identification
The goal of our model is to enforce certain unified policy control for consumer’s service by means of grouping the consumer’s devices for management.
This group can be configured in the subscription server of the operator.
Subscriber ID used for unified service management can be constructed based on the requirements of Subscriber ID:
  is assigned & configured by the ISP or operators
  determine which traffic policy such as QoS are enforced by the nodes inside the network
  is combined with the subscriber information
  may correspond to the device identifiers, such as ISIM, etc.
  should be kept unchanged in the Carrier Grade Network Address Translation (CGN) devices
The devices of the consumer and the operator must have the consistent ID for the same management group.
Use of Subscriber ID should enable access to the network and applications including third-party service without additional authentication.
2012/11/6
6
FMC BoF IETF 85 Atlanta

## Slide 7: Group Identification: Technical Issues
Two different types of identifiers play an important role in this case:
  Device Identifier:
    the Device Identifier is used to indicate each individual devices for the customer
    should be kept unchanged in the Carrier Grade Network Address Translation (CGNs)
    the device identifier should be unchanged or updated in case of roaming among different Access Points or Home Gateways.
  Subscriber Identifier:
    is used to indicate a customer under the same policy, e.g. accounting policy, priority profile, etc.
    one Subscriber Identifier may correspondent to multiple Device Identifiers
2012/11/6
7
FMC BoF IETF 85 Atlanta

## Slide 8: Requirement #2: Requirements for UE Mobility in Fixed IP Network
Mobility Requirement:
Regarding the requirements for MN (Mobile Node) mobility in fixed IP networks two use cases can be distinguished:
  mobility between different access technologies e.g. WiFi and 3 GPP
  mobile node MN mobility in a WiFi scenario
The following are the requirements for the User Equipment Mobility in Fixed IP Network:
  Requirement for handover between networks while the session is active according to the network status with the change in the MN attachment.
  Mechanisms and interfaces between operators or access networks SHOULD be deployed to manage the mobility of the traffic flows of their users.
  Mobility should be enabled whether or not coverage areas overlap.
  Differentiated Services (QoS) for the mobile device (MN) should be provided to ensure service guarantee when device is roaming.
  Connectivity status of the MN should be reported to the fixed IP edge router.
2012/11/6
8
FMC BoF IETF 85 Atlanta

## Slide 9: Summary
Strong requirements on Group/Subscriber Identification.
  Challenge is to transmit the Group/Subscriber ID to the fixed IP network.
Strong requirements on support of MN mobility in fixed IP network.
  Challenge is to transmit MN connectivity status to the fixed IP network.
Benefit of this solution will be seamless connectivity and service provisioning to the fixed IP network improving resource allocation and QoS provisioning.
Improve user experience and reduce Capex/Opex for operators.
IETF is strongly encouraged to work on these issues.
2012/11/6
9
FMC BoF IETF 85 Atlanta