## Slide 1: Problem Statement
FMC BoF at IETF 85
draft-xue-intarea-fmc-ps-02
November 6, 2012, Atlanta, US

## Slide 2
Our Scenarios
Hot Spot
Home
Game/Video(Skype etc.)
Remote education
Cloud
VoD or Live video
Operators Service & Internet
WiFi
Internet/Meeting, etc
Cellular
Within coverage area , the internet, VPN or operator’s service must be guaranteed
High BW guaranteed for smart phone
Fixed
QoS and BW adjustable based on the traffic status;
HD Video/QQ/MSN/Game
VPN Service
Cellular
WiFi
Internet service

## Slide 3: Our Architecture
UTRAN
E-UTRAN
GERAN
BPCF
BBF AAA
Cellular
Fixed Network
RG
Operator’s Service
Internet
Public WiFi
……
Core Network
IP Edge
NAT
Policy Control

## Slide 4: Problem Statement Use Case 1 – Why Group ID?
  Service Quality (QoS) for subscriber should be guaranteed, no matter which type of device, so we need to bind all the devices belonging to one subscriber to one group
  All the devices belonging to one subscriber should be charging as one bill
  Application switching among different devices belonging to one group
UTRAN
E-UTRAN
GERAN
BPCF
BBF AAA
Cellular
Fixed Network
RG
Operator’s Service
Internet
Public WiFi
……
Core Network
IP Edge
NAT
Policy Control
Uniform traffic policy based on Group
Group based Charging

## Slide 5
Application for Use Case 1-Uniform Policy Control
GGSN/PGW
Phone
PAD/PDA
PC
Multimedia
Fixed
Access
My service is guaranteed, even different access and different devices.
I am the subscriber of operator X. My service control should be confirmed.
Mobile Access
Devices managed as Group
Ann
Application: Bandwidth sharing, Application mobility, etc.

## Slide 6: Use Case 1 – Protocol Issues
IP edge is the policy enforcement point for FMC architecture.
To enforcement policy, the first thing is to recognize the traffic, which means to base on the IP packet, the IP edge should enforce right policy for special group.
We need to transmit the group ID using IP layer protocols
Fixed Network
Internet
UE1
AP
&
RG
IP Edge
Mobile Network
UE2
Mobile Edge
UE3
Group
Policy Control
IP packet

## Slide 7: Use Case 1 – Solution Approaches
Embed Group Identifier in network layer, so that different nodes in the network can make use of it.
  Subscriber/Group ID can be transmitted in IP layers as option IPv4 header or IPv6 header
  ICMP can be used
  UDP can be used
Protocol work in IETF is needed.

## Slide 8: Problem Statement Use Case 2 - UE mobility in IP network
Issues:
  Fixed network does not track devices
  Devices connected to Wi-Fi come and go, so their status must be tracked
  Mobility tracking should be enabled in hot spot or home WiFi access network
UTRAN
E-UTRAN
GERAN
BPCF
BBF AAA
Cellular
Fixed Network
RG
Operator’s Service
Internet
Public WiFi
Core Network
IP Edge
NAT
Policy Control
…
…
Should recognize UE is in the coverage or not

## Slide 9: Application for Use Case 2 –Resource management
IP edge router
Phone
The IP edge router should adjust the load in the network for the roaming devices.
  Fixed Access
Fixed
Access
Phone
Phone
PAD/PDA
IP edge router

## Slide 10: Use Case 2 – Protocol Issues
Fixed IP network edge routers need to signaling protocol to report the connectivity status of the devices;
Access points need to transmit the status via protocols
Fixed Network
Internet
UE1
AP
&
RG
IP Edge
Mobile Network
UE2
Mobile Edge

## Slide 11: Use Case 2 – Solution Approaches
New extension based on CAPWAP.
  Connectivity status transmitted via protocols such as CAPWAP.
  New signaling protocol.
Protocol work in IETF is needed.

## Slide 12
Thank You