## Slide 1: Host Identification: Scenarios draft-boucadair-intarea-host-identifier-scenarios-01 IETF 85-Atlanta, November 2012
M. Boucadair, S. Durel, D. Binet & T. Reddy

## Slide 2: Background
Host identification issue was raised in the BBF/3GPP FMC Workshop (November 2011)
  http://www.3gpp.org/ftp/workshop/2011-11-09_3GPP_BBF_SFO/Docs/3BF-11046.zip
  “Encourage IETF work on mechanisms to enable identifying individual UEs behind NAT/RGs”
Some progress was made in intarea WG
  RFC 6269: listing issues encountered in address sharing context including implicit host identification (June 2011)
  http://tools.ietf.org/html/draft-ietf-intarea-nat-reveal-analysis: analyzed 9 candidate solutions (Work started in March 2011)

## Slide 3: So, what is still missing?
Solution specification?
  A gap analysis is needed from the FMC community
Is this issue specific to the so called FMC use case?
This draft aims to provide a big picture overview of scenarios where the host identification issue is encountered
  No solution-related discussion is included in the draft

## Slide 4: Is this issue specific to the so called FMC use case?
No
9 scenarios are identified so far:
  CGN
  A+P/MAP
  Application Proxies
  UE behind a NATing RG
  FAP behind a NATing RG
  Applying policies when a NAT is located in the boundary of the mobile network
  Correlating between internal IP address:port and external IP address:port (PDP/PEP in NATed context)
  Access to some cloud services when a NAT is in the path
  Assign an IPv6 prefix to a host in the context of Provider Wi-Fi
These are the so called FMC case

## Slide 5: The identified FMC case is deployment-specific
Enforcing the NAT in the RG for a visiting UE will bring all the issues discussed in RFC6269 for the subscriber owning the RG
  Is this acceptable for all service providers?
  The main advantage is to leverage on the NAT in the RG and avoid introducing a CGN in the Provider’s network
  Can be appropriate for community Wi-Fi service

## Slide 6: The identified FMC case is deployment-specific
If the NAT is not enforced in the RG but in the Service Provider’s network
  The customer owning the RG is not impacted by a misbehaving visiting UE
  Still, UEs sharing the same IP address will suffer from the same issues as for the CGN case
In both case (NAT in RG or NAT in Service Provider’s network), the host identification is still problematic

## Slide 7: Generalizing the Problem
The host identification issue is valid for both IPv4 and IPv6
  IPv4
    The causes are address sharing, distinct administrative boundaries, use of tunnels, etc.
    Mainly for applying policies: DSCP remarking, volume-based service offering, blacklist, etc.
    Need to correlate between the external IP address and internal IP address
  IPv6
    For applying policies in the context of NPTv6
    For assigning an IPv6 prefix in some contexts

## Slide 8: Conclusions
Host Identification is a valid technical problem
  For both IPv4 and IPv6
It is encountered in some FMC-related scenarios…but it is not specific to FMC
If the IETF has to conduct additional work on the host identification item, handling the issue with a big picture view is more valuable
  Restricting it to FMC case is not encouraged