## Slide 1: Extension of the MLD proxy functionality to support multiple upstream interfaces <draft-contreras-multimob-multiple-upstreams-00.txt>
Luis M. Contreras
Telefónica I+D
Carlos J. Bernardos
Universidad Carlos III de Madrid (UC3M)
Atlanta, MULTIMOB WG, November 2012
1

## Slide 2: Motivation
85th IETF, Atlanta
The support of multiple upstream interfaces on an MLD proxy functionality has been identified as an opportunity for system optimization
Advantages:
  Traffic routing optimization within the PMIPv6 domain
  Simultaneous support of remote & local multicast subscription
  Avoidance of multi-MLD proxy instances on MAG
Complexity
  Handling of control messages for/from multiple upstreams
  Efficient handling of data traffic for/from multiple upstreams
Purpose
  Requirements identification for supporting multiple upstreams
  Specification of the needed MLD proxy functional extensions
2

## Slide 3: Scenarios of applicability for MULTIMOB
  Listener mobility
    Single MLD proxy instance on MAG
    Remote and local multicast subscription
    Dual subscription to multicast groups during handover
  Source mobility
    Support of remote and direct subscription in basic source mobility
    Direct communication between source and listener associated with distinct LMAs but on the same MAG
    Route optimization support in source mobility for remote subscribers
3
85th IETF, Atlanta

## Slide 4
Summary of needed functionality per scenario
85th IETF, Atlanta
 | Multicast Listener |  |  | Multicast Source |  | 
Functionality | Single MLD proxy (4.1.1) | Remote & Local Subscr. (4.1.2) | Dual Subscr. during HO (4.1.3) | Direct & Remote Subs. (4.2.1) | Listener & Source on MAG (4.2.2) | Route Optimiz. (4.2.3)
Upstream Control Delivery |  |  |  |  |  | 
Downstream Control Delivery |  |  |  |  |  | 
Upstream Data Delivery |  |  |  |  |  | 
Downstream Data Delivery |  |  |  |  |  | 
1:1 MN to Upstream Association |  |  |  |  |  | 
1:N MN to Upstream Association |  |  |  |  |  | 
Upstream i/f selection per mcast group |  |  |  |  |  | 
Upstream i/f selection for all groups |  |  |  |  |  | 
Upstream traffic replication |  |  |  |  |  | 

## Slide 5: Extension of the MLD proxy functionality to support multiple upstream interfaces <draft-contreras-multimob-multiple-upstreams-00.txt>
Backup slides
Applicability Scenarios for MULTIMOB
5

## Slide 6: Listener mobility Single MLD proxy instance on MAG
6
85th IETF, Atlanta
Orange
LMA
Green
LMA
Green
MLD
proxy
Orange
MLD
proxy
Orange MNs
Green MNs
MAG
Orange
LMA
Green
LMA
MLD
proxy with
multiple
upstreams
Orange MNs
Green MNs
MAG

## Slide 7: Listener mobility Remote and local multicast subscription
7
85th IETF, Atlanta
MTMA
Multicast
Router
MLD
proxy with
multiple
upstreams
MAG
PMIPv6
domain
(Sremote, G1)
(Slocal, G2)

## Slide 8: Listener mobility Dual subscription to multicast groups during handover
MN
(S, G)
8
85th IETF, Atlanta
LMA
pMAG
nMAG
(S, G)
MN
Handover assisted by some adaptation of FPMIPv6 protocol for multicast traffic
(e.g., draft-schmidt-multimob-fmipv6-pfmipv6-multicast)
Content
Request
Content
Request
X
(S, G)

## Slide 9: Source mobility Support of remote and direct subscription in basic source mobility
9
85th IETF, Atlanta
LMA
Multicast
Router
MLD
proxy with
multiple
upstreams
MAG
PMIPv6
domain
(SMN, Ga)
(SMN, Ga)
MN
(SMN, Ga)

## Slide 10
MN
(S, G)
10
85th IETF, Atlanta
LMA
pMAG
nMAG
(S, G)
MN
(S, G)
Source mobility Route optimization support in source mobility for remote subscribers
MN
PMIPv6
domain
(S, G)

## Slide 11: Source mobility Direct communication between source and listener associated with distinct LMAs but on the same MAG
11
85th IETF, Atlanta
Orange
LMA
Green
LMA
MLD proxy with
multiple upstreams
MAG
(SMN, Ga)
(SMN, Ga)
MN
(SMN, Ga)
MN