## Slide 1: Multicast Routing Optimization by PIM-SM with PMIPv6 draft-asaeda-multimob-pmip6-extension-11
Hitoshi Asaeda
Pierrick Seite
85th IETF, November 2012, Atlanta, USA

## Slide 2: Overview
Multicast route optimization done by PIM-SM routing protocol running on both LMA and MAG in PMIPv6
  Source and/or RP addresses selected by the RPF lookup algorithm
    No tunnel convergence problem
    Optimized routing
  Both ASM and SSM supported
Localized routing and direct routing support
Mobility support
  Most of handover scenarios (mentioned until -10) were deleted as they were duplicated with a handover draft
  Only handover using MN’s policy profile mentioned

## Slide 3: Basic Data Flow – Example
MAG and LMA act as PIM-SM routers
  Upstream IF for (S1,G1) is MAG’s M-Tunnel IF
  Upstream IF for (S2,G2) is MAG’s physical IF (i.e., direct routing without any tunnel)
MN1
MN2
MAG
LMA
MLD Report
(S2,G2)
PIM join
M-Tunnel
MLD Report
(S1,G1)
(S1,G1)
PIM join
PIM join
(S2,G2)

## Slide 4: M-Tunnel (GRE Tunnel)
  M-Tunnel is a GRE tunnel manually set up at MAG
    Dedicated for multicast packet transmission
    GRE key is manually configured by operation, or dynamically negotiated with RFC5845
    Tunnel end points can be;
      LMA
      Other MAG (for localized routing)
      PIM-SM routers in a local domain (for direct routing via tunneling)
    Multicast routes with M-Tunnel are referred by MRIB

## Slide 5: M-Tunnel Configuration (Basic operation)
MAG uses an M-Tunnel (attached to LMA) as an upstream link for external multicast packets
  E.g., ip mroute 0.0.0.0 0.0.0.0 gre0

## Slide 6: Example 1: Basic Operation
Fixed Internet
LMA1
MAG2
Src
MN
M-Tunnel
PIM-SM
router
PIM Join
LMA2
MAG1
PMIPv6-Domain
MN
ip mroute 0.0.0.0 0.0.0.0 gre0
MN
MN

## Slide 7: M-Tunnel Configuration (Advanced operation)
Operators may want to set up multiple upstream interfaces at MAG to support different scenarios;
  Case 1: Remote contents from a single LMA and local contents via direct routes (static or dynamic)
  Case 2: Remote contents from different LMAs for different prefixes
  Case 3: Remote contents from different LMAs managed by ECMP (not for load balancing, but for load split)

## Slide 8: Advanced Operation – 1: M-Tunnel + Direct Routing
Fixed Internet
LMA1
MAG2
Src
MN
M-Tunnel
PIM-SM
router
PIM Join
LMA2
MAG1
PMIPv6-Domain
MN
ip mroute 0.0.0.0 0.0.0.0 gre0
ip mroute 1.1.0.0 255.255.0.0 fas1
MN
MN
Src
MR
1.1.1.10

## Slide 9: Advanced Operation – 2: Multiple M-Tunnels for Different Prefixes
Fixed Internet
LMA1
MAG2
Src
MN
MN
MN
M-Tunnel
PIM Join
MAG1
PMIPv6-Domain
MN
PIM-SM
router
ip mroute 0.0.0.0 0.0.0.0 gre0
ip mroute 11.1.0.0 255.255.0.0 gre1
ip mroute 20.0.0.0 255.0.0.0 gre1
gre0
gre1
11.1/16
20/8
LMA2
Src
11.1.1.10

## Slide 10: Advanced Operation – 3: Multiple M-Tunnels by ECMP
Fixed Internet
LMA1
MAG2
Src
MN
MN
MN
M-Tunnel
PIM Join
LMA2
MAG1
PMIPv6-Domain
MN
Src
MR
PIM-SM
router
ip multicast multipath s-g-hash next-hop
gre0
gre1
(S1,G1)
(S2,G2)

## Slide 11: Mobility Support
Mobility support (i.e. seamless handover)
  Ex. 1: With Policy Profile
    When MN’s subscribing channel list is always maintained
  Ex. 2: With multicast extended PBU/PBA
    draft-ietf-multimob-fast-handover-03
  Ex. 3: With multicast extended CXTP
    draft-vonhugo-multimob-cxtp-extension-02

## Slide 12: Handover Scenario – With PBU (DeReg) and PBA
MN p-MAG LMA n-MAG
| | | |
|----- MLD Report ---->| | |
| |====M-Tunnel(PIM join)====>| |
| | |---> PIM join |
|<---------------------|<===M-Tunnel(Multi.data)===| |
| | | |
Detach | | |
| MN detachment event | |
| |------- DeReg PBU-M ------>| |
| | (Acquire multicast channel |
| | information for MN-ID) |
| | Accept PBU |
| |<---------- PBA -----------| |
Attach | | |
| | | MN attachment event (Acquire MN-ID)
|------------------------------------ RS ------------------------------------->|
| | |--------- PBU -----------|
| | |---------- PBA-M --------->|
| | | (Acquire multicast channel
| | | information for MN-ID)
| | |<=== M-Tunnel(PIM join)====|
|<----------------------------------- RA --------------------------------------|
| | |===M-Tunnel(Multi.data)===>|
|<--------------------------------- Multicast data ----------------------------|
| | | |

## Slide 13: Handover Scenario – Direct Routing
MN p-MAG LMA n-MAG
| | | |
|----- MLD Report ---->| | |
| |---> PIM join | |
|<-- Multicast data ---| | |
| | | |
Detach | | |
| MN detachment event | |
| |------- DeReg PBU-M ------>| |
| | (Acquire multicast channel |
| | information for MN-ID) |
| | Accept PBU |
| |<---------- PBA -----------| |
Attach | | |
| | | MN attachment event (Acquire MN-ID)
|------------------------------------ RS ------------------------------------->|
| | |--------- PBU -----------|
| | |---------- PBA-M --------->|
| | | (Acquire multicast channel
| | | information for MN-ID) |
| | | |---> PIM join
|<----------------------------------- RA --------------------------------------|
|<----------------------------------- Multicast data --------------------------|
| | | |

## Slide 14: Conclusion
This draft provides “Multicast Routing Optimization by PIM-SM with PMIPv6”
WG interests this optimization?