## Slide 1: Mobile Multicast Sender Support in PMIPv6 Domains draft-ietf-multimob-pmipv6-source-02
Thomas C. Schmidt
t.schmidt@ieee.org
HAW Hamburg

## Slide 2: Objective of the Draft
Define Multicast Source Mobility for PMIP
Three Basic Multicast Scenarios:
Base-line approach compliant to RFC 6224:
  Simple, directly reflects PMIP routing
Direct Multicast Distribution
  Based on Proxies, PIM-S(S)M or BIDIR PIM
Optimized Source Mobility
  Extended Proxies for traffic optimization

## Slide 3: Document History
Version draft-ietf-multimob-pmipv6-source-01
  Presented in Vancouver
  Some WG feedback, pointers on issues by Stig
Current version draft-ietf-multimob-pmipv6-source-02
  Added clarifications in response to WG feedback.
  Fixed issues.
  Completed specification of multiple upstream proxy.
  Clarified proxy peering operations.

## Slide 4: 3. Optimized Source Mobility
Scenario: Proxies at MAGs
Objective: Optimize traffic exchange from a local MAG - including policy implementations
Requirements:
  Unique coverage of receivers
  Prevention of Routing Loops
Multiple upstream proxy for sources (MUIMP)
  Traffic forwarded to multiple LMAs
Proxy Peering Interface (PPI)
  Horizontal traffic exchange between proxy instances

## Slide 5: 3.1 Multiple Upstream Proxy
Single Proxy instance with multiple upstreams deployed at MAG
Objectives:
  Distribute Multicast services according to local policies
  Unambiguously guide traffic to upstream interfaces
Approach:
  Route according to a filter table

## Slide 6: 3.1 Filter Table for MUIMP
Multicast State | Upstream Interface
(S1local , *) | UP-IF1
(*,G1) | UP-IF2
(S2,G2) | UP-IF3
(*,*) | UP-IF1
Processing: Apply first matching filter
For Sources:
  Can express PMIP policy-based routing
For Receivers:
  Can sort according to Groups/Channels, but not policies
Policy-based Upstream Routing
Group / Channel
Specific Routing
Remaining Default

## Slide 7: 3.1 Filter-based Routing for MUIMP – Typical Use Cases
Express PMIP policies (for sources only)
Separate local and remote services:
  Have selected local channels, keep default remote, or
  Provide default services locally, provide selected channels from the remote
Can do many more complicated things … but the goal is to support straight-forward needs

## Slide 8: 3.2 Proxy Peering (update)
Defines new interface type: Peering
  Established between any two proxy instances for shortcutting traffic
  Silent virtual link in regular proxy operations
Fixed MLD details:
  IGMP2/MLD1: Install incoming filter at MAGs, only
  IGMPv3/MLDv2: Source-specific traffic selection (ASM and SSM)
Source-specific signaling will avoid duplicate traffic

## Slide 9: Future Steps
Some (few) editorial improvements needed
Improve according to WG feedback
Elaborate security section
Add source operations for fast handover solutions ? … (in case the WG will identify a reasonable path to do fast handovers )

## Slide 10
Questions?