## Slide 1: A Taxonomy of Grouping Semantics for RTP Sources draft-lennox-raiarea-rtp-grouping-taxonomy-00 AVTExt, IETF 86, 15 March 2013
Jonathan Lennox jonathan@vidyo.com
Kevin Gross kevin.gross@avanw.com
Your name here!

## Slide 2: Background
At the Atlanta IETF, discussion of the SRCNAME draft ratholed on confusion on several topics:
  What a “source” is
  What terms to use for various concepts in RTP
We had an ad-hoc breakout meeting afterwards to discuss these issues
This document is a result of that discussion
  Didn’t have as many contributions as I’d hoped...
We also had a breakout this Monday

## Slide 3: Naming and Definitions
This draft tries to:
  Come up with good names for important concepts
  Come up with precise definitions for them
  Still a lot of work to do
    Most of the names are tentative.
    Suggestions welcome – but not at the mic, please!
Issues with naming:
  A lot of terms are already used, in contradictory ways.
    “Stream” is the worst offender here

## Slide 4: Basic Concepts (1): Synchronization Source
Synchronization Source
  “the source of a stream of RTP packets, identified by a 32-bit numeric SSRC identifier carried in the RTP header.”
  Most commonly, a single flow of encoded media, for a single decoding process.
  Can also be used for repair flows, sub-flows of a layered encoding, etc.

## Slide 5: Basic Concepts (2): Sessions
RTP Session
  A communications channel among a group of participants communicating via RTP
Multimedia Session
  A group of concurrent, associated RTP sessions

## Slide 6: Basic Concepts (3): Media Source Output
Media Source Output
  A unique piece of media that can be rendered to a human
  Can be available in multiple formats, but intended to provide the same experience, modulo quality.
  Can be composed of several synchronization sources, possibly in different RTP sessions (always the same multimedia session).
  Probably maps to a CLUE Capture (or Encoding?) or a WebRTC RtcMediaStreamTrack (or its source?).
  (Called Media Source in the draft; the term Media Source Output was suggested on Monday.)

## Slide 7: Group relationship types
Relationships among media sources
  Synchronization contexts (identified by CNAME)
  CLUE Scenes (and their substructures)
  WebRTC MediaStreams
  Clock source
Alternative representations of media sources
  Simulcast
  Multi-Stream Transmission (MST) of Layered Codecs
Robustness and Repair
  Forward Error Correction
  Retransmission

## Slide 8: Path forward
We need good names and definitions for concepts
We may need more concepts defined
We need to know where to discuss this work
  rai area mailing list?
We need more contributors!