## Slide 1
Traffic Management
Benchmarking Framework
IETF 86 Orlando
Barry Constantine
barry.constantine@jdsu.com
Tim Copley
timothy.copley@level3.com
Ram Krishnan
ramk@brocade.com

## Slide 2: Traffic Management Benchmarking Overview
Could be an extension of RFC 2544 benchmarking into traffic management functionality
  Classification / Prioritization
  Policing
  Buffering
  Queuing / Scheduling
  Shaping
In addition to packet based testing, would utilize “application test patterns” in order to fully characterize the performance of the device under bursty traffic conditions

## Slide 3: Status of Personal Submission
Received extensive comments from three (3) reviewers
  Overall comments were very supportive of this work
Summary of comments:
  Test the DUT with multiple flows during each of the test types; for example, queue tests need each type of queue exercised in parallel
  In addition to observed packet performance (i.e. drops), verify that the DUT counters are accurate
  Need to address multiple port test cases
  Add TCP layer testing to the Policer benchmarking (in addition to stateless traffic tests)
  Remove the misused “QoS” term throughout document

## Slide 4: Discussion of Benchmark vs. Functional Test
Al Morton made some comments (as chair) concerning the nature of a functional test versus black-box benchmark
  “Inherently, that testing includes the "functional" test that you are seeking now (If I configure 64kbps CBR, does the DUT enforce/achieve that limit)”
Language in the draft will be augmented to align with the BMWG charter
  Clearly state that performance metrics will be measured to compare vendor performance

## Slide 5: Next Steps for the Traffic Management Draft
We seek the BMWG to formally adopt this personal submission as a chartered draft work
Work intensely on the next revision(s) to incorporate the excellent comments that we received