## Slide 1: draft-ali-ccamp-rsvp-te-include-route-03.txt CCAMP – IETF 86 – Orlando March 2013
  Zafar Ali
  Clarence Filsfils
  Gabriele Maria Galimberti
  Ori Gerstel
  Kenji Kumaki
  Rüdiger Kunze
  George Swallow
  Cisco Systems
  Cisco Systems
  Cisco Systems
  Cisco Systems
  KDDI Corporation
  Deutsche Telekom AG
  Cisco Systems

## Slide 2: Overall Problem Space
UNI-C
UNI-N
NNI
NNI
UNI-C
UNI-N
A TE headend may have no visibility across UNI or NNI boundarys
This draft is to allow such a headend to request commonality between paths

## Slide 3: Homogeneity and Fate-sharing
draft-ali-ccamp-rsvp-te-include-route
Requirement is to have two LPSs to follow same route:
  Fate Sharing.
  Homogeneous Attributes: E.g., when LSPs are bundled together, it is often required that they have same delay and DV characteristics.
The ingress node requires certain nodes, links, or path of another LSP to be explicitly included
  This derives, for instance, from an overall link diversity plan

## Slide 4: Homogeneity and Fate-sharing(2)
Ingress node may lack sufficient topological knowledge
It there must form an ERO with loose hop(s)
It cannot divide those loose hop(s) into a proper sequence of strict or a sequence of finer-grained loose hops (e.g., in inter-domain and GMPLS overlay networks).
UNI-C
UNI-N
NNI
NNI
UNI-C
UNI-N

## Slide 5: Homogeneity and Fate-sharing: Solution
Explicit Inclusion Route Subobject (EIRS)
  A new ERO subobject type
  Indicates an inclusion between a pair of explicit or abstract nodes
Encoding and processing rules are similar to Explicit Exclusion Route Subobject (EXRS) subobject of ERO defined in [RFC4874],
  (the exception being include vs. exclude semantics)
Subobjects supported by XRO/ EXRS are supported
  i.e., inclusion of links, nodes, tunnel / LSP, unnumbered interfaces, etc.
  In this draft, dropped SRLGs

## Slide 6: SRLG Issues
We naïvely incorporated all the subobjects of the XRO
  Ran into difficulty writing the processing rules for SRLGs
A processing node may not be able to fully expand a loose hop an explicit ERO
  In such an event it will need to insert another loose hop
  What if any SRLGs should it include?
The authors do not find inclusion of an SRLG as needed functionality
Happy to entertain the opinions and processing rules that others may want to supply

## Slide 7: Next Steps
Authors consider draft mature enough to call for WG adoption