## Slide 1
SRLG Issues and Potential Solutions
CCAMP – IETF 86 – Orlando
swallow@cisco.com
Notes: 1

## Slide 2: Current SRLGs
A single 32 bit flat (unstructured) number space
  Administrated by the organization responsible for a particular network
  If any structure exists, it is specific to the organization
Authors have gotten input from many folks
  All agree there is a problem
  Various opinions on what is most problematic
  Various opinions on what should be done
This presentation (more so than the draft) is to stimulate wider discussion

## Slide 3: Multi-layer multi-domain Identification
SRLGs in multi-domain and multilayer networks are likely not unique
When crossing administrative domains risk of collisions exits
Potential solution: Add an ASN

## Slide 4: Path Diversity
When a diverse path cannot be found, some would like a “Maximally Diverse Path”
With current information, this means select a path with the fewest SRLGs in common
Availability of resources in networks vary widely
  Particularly true in optical networks
Ideally “Maximally Diverse Path” between LSPs A and B would be Max(Availability(LSP A or LSP B))

## Slide 5: Availability Requirements
Client may request specific availability for (UNI) circuits provided by the SP (e.g., five-nines of SLA).
SP may use client’s circuit availability requirement as a constraint on what resources can be used for the circuit

## Slide 6: SRLG Availability
Associate an availability with the resource identified by the SRLG
Availability = MTBF/(MTBF+MTTR).
Availability can be compactly represented in discrete levels, e.g. # of 9’s

## Slide 7: Multilayer Considerations
Not all the information at layer 0 may be interesting at layer 3
  In fact the majority of SRLGs in an optical network may not be interesting to IP/MPLS networks
Some form of abstraction / reduction is needed
Possibilities
  Filtering
  Summarization by mapping
  Other abstract representation?
  Perhaps a combination is needed

## Slide 8: SRLG Scaling
Amplifier site
Multi Degree Site
Multi Degree Site direction
Span 1
Span 2
Multi Degree Site + Regen
Span 1
Span 2
Span 3
Span 1
Span 2
Span 1
Span 2
Span 1
Span 2
Span 3
Span 4
Span 5
A
B
C
Span 1
Span 2
Span 3
D
A
B
C
Multi Degree Site + Regen
D to B is Regen
Multi Degree Site
Amplifier site
Multi Degree Site
OMS
OMS
OMS
Site A
Site B
Site C
Site D
An SP may assign an SRLG for each risk. We can easily have hundreds of SRLGs for LSPs transiting the domain it operates.
Some SRLGs that are important to one layer, may not be important for another layer.

## Slide 9: Filtering
Availability information
Type of equipment
Operator assigned priority

## Slide 10: SRLG Type
Enables Examination of a resource type associated with an SRLG.
May be used to filter SRLG information in multi-domain/ multi-layer networks.
Many possiblities
  OMS (between adjacent ROADMs – a.k.a. line)
  OTS (between adjacent amplifiers – a.k.a. span)
  Fiber Duct: Conduit carrying fibers (which represent optical sections).
  Building: Building hosting multiple network elements, and represents a common risk.
  Optical NE: Amplifier, ROADM or other optical NE used along an optical TE link.
  Power feed: a common power source feeding multiple NEs
  Geographic region: an area susceptible to a disaster such as earthquake or flood.
  ODU path – can be nested
  ODU line (between OTN XCs)
  OTU (between regens)
  More to be added in future revision.

## Slide 11: Type issues
A small space may be overly constrained
Too large a space leads to entropy, i.e.
  Overlapping values
  Overly specific
Standardized Registry or simply operator assigned?
  Operator assigned would not help in true multi-domain situations (including those arising through acquisitions
  May also complicate the multilayer case
  Standardized Registry hard to administrate if it is small but as noted the problems of a large space have been noted
But a registry should not be ruled out
  Space divided between standard, FCFS, and private

## Slide 12: SRLG Priority
Operator assigned priority associated with the SRLG
  Could be automatically assigned based on type
Number of levels need not be large
Potential mechanism for SRLG filtration
  For example, in a multi-layer network, only higher priority SRLGs may be exposed to the client layer
  Setting of priorities could be a cooperative effort between transport and packet departments

## Slide 13: Information flows and repositories
How should the information be collected
Clearly
  SRLGs numbers needed to be collected
  For inter-domain, a means of knowing when you cross an AS boundary
Other information (priority, type, availability)
  Are these sufficiently stable that they could exist off-line and be made available by distributing config-lets
  Is it worth saving the bits?

## Slide 14: Next Steps
Encourage discussion on the list
Please offer feedback
Update draft for Berlin