## Slide 1: RSVP-TE Based MPLS LI & LB
jie.dong@huawei.com
mach.chen@huawei.com
lizhenqiang@chinamobile.com
daniele.ceccarelli@ericsson.com (new co-author)
IETF86 CCAMP Mar. 2013 Orlando
draft-dong-ccamp-rsvp-te-mpls-tp-li-lb-05

## Slide 2
LI&LB are useful OAM functions in a transport network
  The lock function enables an operator to lock a transport path such that it does not carry client traffic, but can continue to carry OAM messages and may carry test traffic.
  The loopback function allows an operator to set a specific node on the transport path into loopback mode such that it returns all received data.
The LI&LB requirement defined in RFC 5860, and NMS based LI & LB defined in RFC 6435
  Suitable for the scenario where no control plane used
This document introduces a general control plane based LI&LB
  LI&LB affect the data plane of the LSP
  Control plane based LI&LB can ensure control plane & data plane consistency
Background

## Slide 3: Solution Overview
Lock Instruct
Loopback
LER1
LSR1
LER2
LSR2
Perform Lock operation
Path with A set
Resv (success) or
PathErr (failure)
LER1
LSR1
LER2
LSR2
3.Perform Loopback Operation
1. Path with Loopback bit set
Resv (success) or
PathErr (failure)
2. Address to LSR2 by Per-Hop attribute mechanisms
Notes: Enter Loopback
  Sending MEP: Path message with Loopback bit set
    Target to specific Node by Extended ERO Object
  Receiving MIP/MEP:
    Check the Extended ERO to determine whether it is the target node
    Success: Resv message with Loopback bit (In RRO Attribute subobject)
    Failure: Patherr message with new OAM Error Value “Loopback Failure”
Exit Loopback
  Sending MEP: Path message with Loopback bit cleared
  Receiving MIP/MEP:
    Success: Resv message with Loopback bit cleared
    Failure: Patherr message with new OAM Error Value “Exit Loopback Failure”
Enter Loopback
  Sending MEP: Path message with Loopback bit set
    Target to specific Node by Extended ERO Object
  Receiving MIP/MEP:
    Check the Extended ERO to determine whether it is the target node
    Success: Resv message with Loopback bit (In RRO Attribute subobject)
    Failure: Patherr message with new OAM Error Value “Loopback Failure”
Exit Loopback
  Sending MEP: Path message with Loopback bit cleared
  Receiving MIP/MEP:
    Success: Resv message with Loopback bit cleared
    Failure: Patherr message with new OAM Error Value “Exit Loopback Failure”

## Slide 4
Pre-version-05
  Mainly designed for MPLS-TP network
  Complementary to the NMS based LI & LB
Updates in version-05
  Generalize the application scope (according to Lou’s suggestion)
    To both MPLS-TP and non-MPLS-TP scenarios
  Updated the terminologies and relevant description to align with the conventions of CCAMP
  Editorial changes
Updates

## Slide 5
Authors think this is ready to be adopted as a WG document
Next Steps