## Slide 1: RSVP-TE Extensions for LSP Inquiry draft-ali-ccamp-lsp-inquiry-00.txt
Author list:
  Zafar Ali (zali@cisco.com) - Presenter
  George Swallow (swallow@cisco.com)
  Clarence Filsfils (cfilsfil@cisco.com)
  Matt Hartley (mhartley@cisco.com)
  Ori Gerstel (ogerstel@cisco.com)
86th IETF, CCAMP WG, Orlando, FL, USA (March 2013)

## Slide 2: Outline
Requirements and Scope
Problem Statement
Solution
Next Steps

## Slide 3: Requirements and Scope
In packet networks LSRs can easily double book resources (bandwidth, labels, etc.) for current and reopt LSPs and can share physical resource and install cross-connect for both LSPs at the same time.
Optical network has limitation w.r.t. resource and cross-connect sharing between existing and reopt LSPs.
Applicable to inter-domain, overlay, as well as for peer models.
The inquiry procedure can also be used as a probing mechanism (outside the context of re-optimization).
15454
OXC2
Router 1
Router 2
GMPLS Network
OXC3
OXC1
OXC4
1
OXC5
OXC6
1
1
3

## Slide 4: What is Inquiry?
Inquiry refers to a way to “flag” optical network to allow sharing of resources (link, wavelengths) between current and inquiry LSPs – without installing cross-connect for inquiry LSP (i.e., without affecting traffic on the existing lsp).
There is a need for installing cross-connect when reopt (inquiry) LSP is considered as “good enough” to move tunnel from current LSP to Reopt (inquiry) LSP.

## Slide 5: Inquiry Procedure – Inquiry with Resource Lock
Ingress LER
Egress LER
Path w/ pre-planned LSP flag = 1 w/ SE [RFC6001 & RFC3209]
Path enquiry response (with
TE Metric, SRLG list, latency, lambda, etc.)
path locked; resources shared
(No xconnect; only in CP)
Periodic/ Manual Reopt/ Probe
Path w/ pre-planned LSP flag = 0 w/ SE
Inquiry LSP Passes Evaluation
Inquiry LSP is
activated in DP
Inquiry LSP is
Activated in CP only (with resource lock)
LSR A
LSR B
Reopt LSP is ready for take traffic

## Slide 6: Inquiry Procedure – inquiry without Resource Lock
Path w/ pre-planned LSP w/o “lock” flag = 1 w/ SE
Path inquiry response (with
TE Metric, SRLG list, latency, lambda, etc.)
path locked; resources shared
(No xconnect; no resource lock in CP)
Path w/ pre-planned LSP flag = 0 w/ SE
Reopt LSP is
activated in DP
Inquiry LSP is
Activated in CP only
(without resource lock).
Path w/ pre-planned LSP flag = 1 w/ SE [RFC6001]
Resv with resource locking
Resources are locked in CP. Still no commitment in DP.
Inquiry LSP is ready for take traffic
Ingress LER
Egress LER
Periodic/ Manual Reopt/Probe
LSR A
LSR B
Inquiry LSP Passes Evaluation
path locked; resources shared
(No xconnect; no resource lock in CP)

## Slide 7: Next Steps
We would like to make this draft a WG Document.

## Slide 8
Thank You.