## Slide 1: Information Model for Wavelength Switched Optical Networks (WSON) with Optical Impairments Validation. draft-martinelli-ccamp-wson-iv-info-01
Giovanni Martinelli, Cisco (*)
Moustafa Kattan, Cisco
Gabriele Galimberti, Cisco
Andrea Zanardi, Create-Net

## Slide 2: Optical Impairment Reload
This model was first presented at IETF85 in Atlanta.
It extends the current RWA-WSON approach (current WG documents) to allow Impairment Validation function.
Specific Parameters are strictly derived from ITU documents (G.680, G697 Appendix V).
IETF Context:
  RFC6566, Sec. 4.1.1, Approximated Impairment Calc.
  Not perfect but better than nothing.

## Slide 3: The Computational Model (ITU-G.680)
N1
N2
N3
N4
N5
Wavelength
CURRENT RWA WSON :
It solves Signal Compatibility Problem:
Apply to end points (optical i/f transceivers)
Use of Optical Interface Class (i.e. ITU Application Codes)
TRANSFER FUNCTIONs
  Parameters: single contribution vs. end-to-end.
  ITU-G.680 transfer functions for: OSNR, CD, PMD/PDL.
  Example:

## Slide 4: G.680 Models (Sec. 9.1): OSNR
NODE 1
NODE 2
NODE N

## Slide 5: G.680 Models (Sec. 9.2): CD
Two approaches to evaluate terms of (9-5)
Worst case
Statistical: means and std deviation may be available
Likely shows wavelength dependency
NODE
LINK

## Slide 6: G.680 Model (Sec. 9.3): PMD/PDL
PMD and PDL have a “per node” component.
PDL available as a computational model, not available as Parameter ID in G.697

## Slide 7: From Computational (ITU) To Information (IETF) Model
For each parameter
  it’s possible to provide a by node/by link contribution,
  there is a simple function to put together all contributions (Sum, …).
No hypothesis are done on how each single contribution is provided (e.g. provisioned, computed, known a priori, ….).
Even if the Computational Model is not perfect allows path computation to choose better paths.

## Slide 8: The Information Model (IETF)
Makes room for a list of parameters:
  Does not look at parameter semantic.
  Does not look at specific transfer functions.
Defines basic building blocks to be added to control plane objects
  Impairment Vector (For Node or Link Information)
  Impairment Matrix (For Node Information)
Generalized from existing RWA-WSON (no I.V.) approach.

## Slide 9: Info Model: Impairment Vector
It’s a list of Optical Parameters.
The list could be extended but currently stick to G.697 Appendix 2.
G.697 is for Monitoring, for the purpose of the Info Model just provide the Parameter Identifiers and encoding.
The encoding draft details how identifiers are mapped.

## Slide 10: G.697 Appendix V

## Slide 11: Info Model: Impairment Matrix
Existing WSON Connectivity Matrix only represents a binary information.
Impairment Matrix extends Conn.Matrix with a set of optical values: the impairment vector.
0 | 1 | 1 | 0 | 
1 |  |  |  | 
1 |  |  |  | 
0 |  |  |  | 
… |  |  |  | 
osnr | Etc. |  | 
MATRIX
VECTOR
Objects defined according to G.697

## Slide 12: Next Steps
Does this approach seem a good way to go?
  Yes: refine (need anyway!), wg adoption, …
  No: suggestions, abandon, …
  Don’t know
There were already two individual drafts: plan to work together.
THANK YOU!

## Slide 13: Q for Q6
Giovanni Martinelli / Gabriele Galimberti
Xiang Zhang / Fatai Zhang / Young Lee

## Slide 14: Questions (1)
What impairment data are relevant/stable for control plane to collect for its path computation and what ITU-T references are good to reference?
Does the IETF Information Model currently represent the G.680 computational model ?
G.697 is used to derive a suitable encoding for parameters (the once currently computed by G.680). Is there any update foreseen on G.697? E.g. PDL is in G.680 not in G.697.

## Slide 15: Questions (2)
Are there new modulation formats under standardizations? They generate new Computational Models? They imply new optical parameters?
Does ITU is working on additional computational models (e.g. coherent technology / Non linear effects / ...)? IETF Information model tries to be generic enough.