## Slide 1: Extension to the Link Management Protocol (LMP/DWDM -rfc4209) for Dense Wavelength Division Multiplexing (DWDM) Optical Line Systems
draft-dharinigert-ccamp-g-698-2-lmp-02.txt
Dharini Hiremagalur Juniper Networks
Gert Grammel Juniper Networks
John E. Drake Juniper Networks
Gabriele Galimberti Cisco Systems
Zafar Ali Cisco Systems
Ruediger Kunze Deutsche Telekom

## Slide 2: Motivation & Problem statement
Motivation
RFC4209 extension to cover the parameters as defined in G. 698.2
draft-dharinigert-ccamp-g-698-2-lmp extensions are in alignment with draft-galikunze-ccamp-g-698-2-snmp-mib
The need of this work has been highlighted during the discussion at IETF-83, IETF-84 and IETF-85
Problem Statement
Correlate and check Link properties of both ends of a link and notify inconsistency.
Extending Link Property correlation for G.698.2 based links
Extend RFC4209 covering Application Codes

## Slide 3: About LMP
RFC4204 (LMP) and RFC4209 (LMP-WDM)
  “For scalability purposes, multiple data links can be combined to form a single traffic engineering (TE) link. Furthermore, the management of TE links is not restricted to in-band messaging, but instead can be done using out-of-band techniques. This document specifies a link management protocol (LMP) that runs between a pair of nodes and is used to manage TE links.”
Currently addressing Transponder based links only
Needs extension for wavelength, optical impairments and transceiver characteristics according to G.698.2 and G.694.1
NON-GOAL: LMP is neither a signaling nor a routing protocol

## Slide 4: RFC 4209 Extended LMP Model
+-------+ Ss +--------+ +--------+ Rs +--------+
| | ----- | | | | ----- | |
| OXC1 | ----- | OLS1 | ===== | OLS2 | ----- | OXC2 |
| | ----- | | | | ----- | |
+--------+ +--------+ +--------+ +---------+
^ ^ ^ ^ ^ ^
| | | | | |
| +-----LMP-----+ +-----LMP-----+ |
| |
+-------------------------------LMP------------------------+
OXC : is an entity that contains transponders
OLS : generic optical system, it can be - Optical mux, Optical demux,
Optical Add Drop Mux, etc
OLS1 to OLS2 : represents the black-Link itself
Rs/Ss : between the OXC1 and the OXC2

## Slide 5: Packet/Optical Networking – An example for an architecture
MPLS
Router
Router
LMP
LMP
3
ITU-T G.698.2
1
NE
NE
Optical NMS
SNMP
SNMP
2
SNMP
2
SNMP
2

## Slide 6: G.698.2-LMP
Goal: LMP correlates the link properties east and west of G.698.2 reference points (Rs / Ss):
  Ensure that both ends match before wavelength is lit-up
How it works for standard application codes:
  When connected, Router and Optical Line System perform discovery procedures and exchange Application codes and BL messages.

## Slide 7: Extended RFC4209 LMP Messages for G.698.2 (1)
The general parameters - BL_General
These are the general parameters as described in [G698.2]
1. Bit-Rate/line coding of optical tributary signals
2. Wavelength - (Tera Hertz) 4 bytes (see RFC6205 sec.3.2 and 3.3 TLV):
Grid / Cannel Spacing / Identifier / n
3. Min Wavelength Range - (Tera Hertz) 4 bytes (see RFC6205 sec.3.2 and 3.3 TLV):
Grid/Cannel Spacing/Identifier/n
4. Max Wavelength Range - (Tera Hertz) 4 bytes (see RFC6205 sec.3.2 and 3.3 TLV):
Grid/Cannel Spacing/Identifier/n
5. BER mantissa - 4 bytes
6. BER exponent - 4 bytes
7. FEC Coding - 1 byte
8. Administrative state - 1 byte
9. Operation state - 1 byte
Black Link ApplicationCode - BL_ApplicationCode
1. Single-channel application codes -- 32 bytes (from [G698.1]/[G698.2]/[G959.1]
2. Vendor Transceiver Class -- 32 bytes

## Slide 8: Extended RFC4209 LMP Messages for G.698.2 (2)
Black Link - BL_Ss
These are the G.698.2 parameters at the Source(Ss reference points
1. Minimum Mean Channel Output Power -(0.1 dbm) 4 bytes
2. Maximum Mean Channel Output Power -(0.1 dbm) 4 bytes
3. Minimum Central Frequency - (THz) 4 bytes (see RFC6205 sec.3.2 and 3.3 TLV): Grid / Cannel Spacing / Identifier / n
4. Maximum Central Frequency - (THz) 4 bytes (see RFC6205 sec.3.2 and 3.3 TLV): Grid / Cannel Spacing / Identifier / n
5. Maximum Spectral Excursion - (0.1 GHz) 4 bytes
6. Maximum Tx Dispersion OSNR Penalty - (0.1 dbm) 4 bytes
7. Current Output Power - (0.1dbm) 4 bytes
8. Status of TX - Status of the Transmit link at OXC - 4 bytes
Black Link - BL_SsRs
These are the G.698.2 parameters for the path (Ss-Rs)
1 Minimum Chromatic Dispersion - (ps/nm) 4 bytes
2. Maximum Chromatic Dispersion -(ps/nm) 4 bytes
3. Minimum Src Optical ReturnLoss -(0.1 db) 4 bytes
4. Maximum Discrete Reflectance Src To Sink - (0.1 db) 4 bytes
5. Maximum Differential Group Delay - (ps) 4 bytes
6. Maximum Polarisation Dependent Loss - (0.1 db) 4 bytes
7. Maximum Inter Channel Crosstalk - (0.1 db) 4 bytes
8. Interferometric Crosstalk - (0.1 db) 4 bytes
9. Optical Path OSNR Penalty - (0.1 db) 4 bytes
10. Fiber type - 1 byte

## Slide 9: Extended RFC4209 LMP Messages for G.698.2 (3)
Black Link - BL_Rs
These are the G.698.2 parameters at the Sink (Rs reference points).
1. Minimum Mean Input Power - (0.1dbm) 4bytes
2. Maximum Mean Input Power - (0.1dbm) 4bytes
3. Minimum OSNR - (0.1dB) 4bytes
4. OSNR Tolerance - (0.1dB) 4bytes
5. Current Input Power at the OXC - (0.1dbm) 4bytes
6. Threshold of the input power at OLS - The power level above which the OLS will not function (0.1dbm) 4bytes
7. Current Optical OSNR (0.1dB)
8 Q factor
9. Post FEC BER Mantissa
10. Post FEC BER Exponent
11. Status of RX - Status of the Receive link at OXC - 2bytes
Black Link - OLS_Status
This message is sent by the OLS to the OXC. It includes the wavelength information and the status of the
1. Wavelength - The wavelength which has been accepted by the OLS (Tera Hertz) 4 bytes. (see RFC6205 sec.3.2 and 3.3 TLV): Grid / Cannel Spacing / Identifier / n
2. Length of the Wavelength Availability Map 1 byte
3. Wavelength Availability bits - variable bits depending on the number of wavelengths available (For eg 96 bits for C-band 50GHz)
(Allocation is in multiples of 1byte - 96 bits - 12 bytes) 0 - wavelength is available, 1 - used - variable length
4. Current Input Power (0.1dbm) 4 bytes - This is the current input power at OLS
5. Delta between output power at the Src(OXC)and Input Power at OLS (0.1dbm) 4 bytes - This is the delta between the input power and the transmitted output power at the OXC (from message 2.2 BL_Src)
6. Threshold of the input power at OLS 4 bytes - This is the power level above which the OLS will not function.
7. Current Output Power (0.1dbm) 4 bytes - This is the transmitted output power at the OLS.
8. Status of Rx link at OLS 2 bytes - Status of the Receive link at the OLS
9. Status of Tx link at OLS 2 bytes - Status of the Transmit link at the OLS

## Slide 10: Draft Changes and Next Steps
  Changes
    Updated revision
      draft-dharinigert-ccamp-g-698-2-lmp-02.txt
  Modified:
    Kept alignment with draft-galikunze-ccamp-g-698-2-snmp-mib-02.txt
    Modified Frequency and Wavelength as per RFC6205 sec.3.2 and 3.3 TLV): Grid / Cannel Spacing / Identifier / n
    Cosmetic changes
Next Steps
  Get ccamp consensus to go for WG status
  Keep alignment with draft-galikunze-ccamp-g-698-2-snmp-mib-02.txt
  Cover the parameter set of G.698.2

## Slide 11: Questions
Does the draft cover all the G.698.2 parameters?
Can Q6 provide guidance on which parameters is work ongoing: 10G, 40G, 100G, 400G, 1T?
What are the provisions in the information model to deal with Transceivers that meet a set of application codes in future? E.g. A standard receiver and a high-sensitivity-receiver that can operate under the same conditions but also in an extended range?