## Slide 1: IETF Note Well
http://www.ietf.org/about/note-well.html:
Any submission to the IETF intended by the Contributor for publication as all or part of an IETF Internet-Draft or RFC and any statement made within the context of an IETF activity is considered an "IETF Contribution". Such statements include oral statements in IETF sessions, as well as written and electronic communications made at any time or place, which are addressed to:
  The IETF plenary session
  The IESG, or any member thereof on behalf of the IESG
  Any IETF mailing list, including the IETF list itself, any working group or design team list, or any other list functioning under IETF auspices
  Any IETF working group or portion thereof
  Any Birds of a Feather (BOF) session
  The IAB or any member thereof on behalf of the IAB
  The RFC Editor or the Internet-Drafts function
All IETF Contributions are subject to the rules of RFC 5378 and RFC 3979 (updated by RFC 4879).
Statements made outside of an IETF session, mailing list or other function, that are clearly not intended to be input to an IETF activity, group or function, are not IETF Contributions in the context of this notice.
Please consult RFC 5378 and RFC 3979 for details.
A participant in any IETF activity is deemed to accept all IETF rules of process, as documented in Best Current Practices RFCs and IESG Statements.
A participant in any IETF activity acknowledges that written, audio and video records of meetings may be made and may be available to the public.

## Slide 2: CCAMP-Q6/15 Questions

## Slide 3: WSON Impairments
Q from Q6 experts: What is the objective of this work?
  G.680 only covers the linear problem, not sufficient for real networks
  Q6 experts unsure if non-linear problem is solvable in standard form (no agreements on parameters)
  Is it to provide incremental solutions?
Short answer: can provide incremental improvement
  (see discussion for details)
86th IETF CCAMP Working Group
3

## Slide 4: WSON Impairments
What impairment data are relevant/stable for control plane to collect for its path computation
  Are the computational approaches defined in G.680 a reasonable basis for our work?
  Is our use of G.680 /G.697 Appendix V defined parameters reasonable?
  Is the modeling approach reasonable?
    [E.g, port based modeling vs fiber-based.]
  What other documents should we be referencing?
  What parameters are we missing?
    [e.g., filter function representation]

## Slide 5: WSON Impairments (cont)
From the morning session:
  Peter: G.697 (Appendix V) is really about monitoring, would it be helpful for the document to also include other parameters needed to characterize a path across the network, e.g., filter function representation?
   Answer from discussion: Yes, we (CCAMP) should send liaison to Q6 to request
86th IETF CCAMP Working Group
5

## Slide 6: WSON Wrap Up
It is possible to use G.680 to incrementally modify control plane to represent linear impairments
  Will have limited applicability (can use to estimate a lower bound e.g. can use to determine what will not work, but can not say it will definitely work)
There may be parameters that would be helpful in non-linear impairment calculations
  CCAMP could propose a list for comment by Q6 experts

## Slide 7: G.698.2 Related
From Q6 experts: Why MIBs?
What parameters are needed to characterize a link?
  With standard application codes
  Without
Are the identified managed parameters
  Reasonable?
    [Why not application codes?]
  Sufficient?
Which parameters should be settable?
  Under which conditions?
86th IETF CCAMP Working Group
7

## Slide 8: Managed parameters
+--------------------------------+---------+-----------------+
| PARAMETERS | Get/Set | Reference |
+---------------------------------------+---------+-----------------+
| Minimum channel spacing | G | G.698.2 S.7.1.1 |
| Bit rate/line coding of opt. trib. | G,S | G.698.2 S.7.1.2 |
| signals | | |
| FEC Coding | G,S | G.975 |
| Maximum bit error ratio (BER) | G | G.698.2 S.7.1.3 |
| Fiber type | G,S | G.698.2 S.7.1.4 |
| Wavelength Range | G | G.694.1 S.6 |
| Wavelength Value | G,S | G.694.1 S.6 |
| Vendor Transceiver Class | G | N.A. |
| Single-channel application codes | G | G.698.2 S.5.3 |
+---------------------------------------+---------+-----------------+
Table 1: General parameters
+---------------------------------------+---------+-----------------+
| PARAMETERS | Get/Set | Reference |
+---------------------------------------+---------+-----------------+
| MAX and min mean channel output power | G,S | G.698.2 S.7.2.1 |
| Min and MAX central frequency | G | G.698.2 S.7.2.2 |
| MAX spectral excursion | G | G.698.2 S.7.2.3 |
| MAX transmitter (residual) disper. | G | G.698.2 S.7.2.7 |
| OSNR penalty | | |
| MAX side mode suppression ratio, min | G | G.698.2 S.7.2.6 |
| channel extinction ratio, Eye mask | | |
| Current Laser Output power | G,S | N.A. |
+---------------------------------------+---------+-----------------+
Table 2: parameters at Ss

## Slide 9: Managed parameters
+---------------------------------------+---------+-----------------+
| PARAMETERS | Get/Set | Reference |
+---------------------------------------+---------+-----------------+
| MAX and min (residual) chromatic | G | G.698.2 S.7.3.2 |
| dispersion | | |
| Min optical return loss at Ss | G | G.698.2 S.7.3.3 |
| MAX discrete reflectance between Ss | G | G.698.2 S.7.3.4 |
| and Rs | | |
| MAX differential group delay | G | G.698.2 S.7.3.5 |
| MAX polarization dependent loss | G | G.698.2 S.7.3.6 |
| MAX inter-channel crosstalk | G | G.698.2 S.7.3.7 |
| MAX interferometric crosstalk | G | G.698.2 S.7.3.8 |
| MAX optical path OSNR penalty | G | G.698.2 S.7.3.9 |
| MAX ripple | G | G.698.2 S.7.3.1 |
+---------------------------------------+---------+-----------------+
Table 3: parameters between Ss and Rs
+---------------------------------------+---------+-----------------+
| PARAMETERS | Get/Set | Reference |
+---------------------------------------+---------+-----------------+
| MAX and min mean input power | G | G.698.2 S.7.4.1 |
| Min optical signal-to-noise ratio | G | G.698.2 S.7.4.2 |
| (OSNR) | | |
| Receiver OSNR tolerance | G | G.698.2 S.7.4.3 |
| MAX reflectance at receiver | G | G.698.2 S.7.4.4 |
+---------------------------------------+---------+-----------------+
Table 4: mandatory parameters at Rs

## Slide 10: G.698.2 Related (cont)
Can Q6 provide guidance on which parameters is work ongoing: 10G, 40G, 100G, 400G, 1T?
How will transceivers that meet a set of application codes (>1) be represented?
  E.g. A receiver that can operate over an extended range
86th IETF CCAMP Working Group
10

## Slide 11: Other Q Related
What future management parameters will be introduced to support:
  Colourless/Directionless/Contentionless ROADMs?
Wrap-up of discussion (also see minutes)
    Some of this, not Q6 questions
    For parameters listed in tables, need to liaison with Q14 (management) and Q9 (equipment) for what parameters are supported by the equipment

## Slide 12: Flexi-Grid Related
Which concepts are well and less well defined?
Which terminology is well and less well defined?
  What should we use as placeholder terminology?
Four Questions (see slides-86-ccamp-29)
  What is the relation between optical signal layer (OCh) and media layer?
  How do we characterize links and nodes?
  Resource allocation
  Additional link properties?
86th IETF CCAMP Working Group
12

## Slide 13: Flexi-Grid Related (cont.)
Super channel
  What is the current view/status on definition of an entity containing more than one frequency slot?
  Based on current view/definition(s), is there any restriction on treating more than one frequency slot as a single entity for control/management plane functions?
  (ref: slides-86-ccamp-34)
Wrap-up of discussion (refer to minutes)
  Terminology still being sorted out, need better term than Super Channel.
86th IETF CCAMP Working Group
13